AutoBase®9

HMI Software for monitoring and process control systems

USER MANUAL

AutoBase®9

All Rights regarding this manual and AutoBase®9 programs are reserved for HanSol Tech. Co., Ltd.

© 1995~2005 Hansol Tech Co., Ltd. All rights reserved.

<Notice> This manual can be changed without previous announcement.

Printed on March 18, 2005

CONTENTS

Chapter 1. General Outlines of Execution Program	1

1.1 Types of Running Program	1

1.2 System Requirements	2

Chapter 2. Monitor Program	5

2.1 Run Monitor Program	5

2.1.1 Using Startup	6

2.2 Whole Figure and Shortcuts Descriptions	6

2.2.1 Whole Figure Descriptions	6

2.2.1.1 Title Bar	6

2.2.1.2 Menu Bar	7

2.2.1.3 Menu Button	7

2.2.1.4 Windows Internal Area	7

2.2.2 Shortcuts Descriptions	7

2.3 View Menu	8

2.3.1 View Graphics	8

2.3.1.1 Graphic Elements related to Analog	9

2.3.1.2 Graphic Elements related to Digital	14

2.3.1.3 Graphic Element related to button	17

2.3.1.4 String Tag	20

2.3.1.5 Graphic Module	21

2.3.1.6 Alarm Window	22

2.3.1.7 Multi-graph	23

2.3.1.8 Multi-trend	24

2.3.1.9 Demand Window	26

2.3.1.10 Milli-Data Window	27

2.3.1.11 Graphic Element related to Window Control.	28

2.3.1.12 Database	29

2.3.1.13 Real-time Test Graph	30

2.3.1.14 XY Graph	30

2.3.1.15 Database Trend	31

2.3.1.16 Display Changes	32

2.3.1.17 Bitmap	32

2.3.1.18 Animation	33

2.3.1.19 Single line text	34

2.3.1.20 Rectangle	34

2.3.1.21 Circle	35

2.3.1.22 Line	35

2.3.1.23 Polygon	36

2.3.1.24 Rounded Rectangle	36

2.3.1.25 Curve	36

2.3.1.26 Clock	36

2.3.1.27 Date	37

2.3.1.28 Background Bitmap	37

2.3.1.29 Background Color	37

2.3.1.30 Group	37

2.3.1.31 Extension of Graphic Element	37

2.3.2 Entire Tags	38

2.3.3 Analog Inputs	40

2.3.3.1 Analog Input Details	44

2.3.3.2 Analog Trend Diagnosis	46

2.3.3.3 Analog Data View	48

2.3.4 Analog Outputs	51

2.3.4.1 Analog Output Details	53

2.3.5 Digital Inputs	54

2.3.5.1 Digital Input Details	56

2.3.5.2 Digital Trend Diagnosis	58

2.3.5.3 Digital Data View	60

2.3.6 Digital Outputs	62

2.3.6.1 Digital Output Details	64

2.3.7 String Tags	65

2.3.8 View Registered Groups	67

2.3.8.1 Detailed View of the Registered Group	69

2.3.9 Alarm Files	70

2.3.9.1 Alarm List View	71

2.3.10 Alarm Events	72

2.3.11 Log Files	74

2.3.11.1 Log List View	75

2.3.12 Scripts	76

2.3.13 Communication Server	78

2.3.14 Reports	78

2.3.15 Demand Controls	80

2.3.16 Milli-Datas View	81

2.3.17 Schedules	83

2.3.18 DB Integrations	86

2.3.19 Navigation	87

2.4 Descriptions by Each Menu	88

2.4.1 File Menu	88

2.4.1.1 Log In	88

2.4.1.2 Log Out	89

2.4.1.3 Write Memo	89

2.4.1.4 Read Memo	90

2.4.1.5 Print Screen	91

2.4.1.6 Save Screen	91

2.4.1.7 Save Selected Screen	92

2.4.1.8 Run Studio	93

2.4.1.9 Exit	93

2.4.2 View	93

2.4.3 Config	94

2.4.3.1 Config Alarm	94

2.4.3.2 Config Font	95

2.4.3.3 Config Colors	95

2.4.3.4 Config Data	96

2.4.3.5 Config Users	97

2.4.3.6 Config Other	98

2.4.3.7 Config Excel Path	99

2.4.3.8 Database	100

2.4.3.9 Schedules	102

2.4.3.10 Automatic Report Print	102

2.4.4 Windows	103

2.4.5 Help	104

2.4.5.1 Help	104

2.4.5.2 UserName?	104

2.4.5.3 Keylock Information	105

2.4.5.4 About?	105

Chapter 3. Communication Server	107

3.1 Communication Server Running	108

3.2 Whole Figure and Shortcuts Descriptions	108

3.2.1 Whole Figure Descriptions	108

3.2.1.1 Title Bar	109

3.2.1.2 Menu Bar	109

3.2.1.3 Menu Button	109

3.2.1.4 Windows Internal Area	109

3.2.2 Shortcuts Descriptions	110

3.3 Descriptions for each Menu	111

3.3.1 File Menu	111

3.3.1.1 Modify Communication Ports	111

3.3.1.2 Bit Write	113

3.3.1.3 Word Write	113

3.3.1.4 Virtual Write	114

3.3.1.5 Exit	114

3.3.2 View Menu Items	114

3.3.2.1 Main Program	115

3.3.2.2 Memory	115

3.3.2.3 Communication Code into Hex	116

3.3.2.4 Communication Code into ASCII	116

3.3.2.5 Port Status	117

3.3.2.6 Network Memory Server	117

3.3.2.7 DLL Protocol Information	119

3.3.3 Config Menu Item	120

3.3.3.1 Options	120

3.3.3.2 Editor Font	121

3.3.3.3 Modem Options	121

3.3.4 Windows Menu Items	121

3.3.5 Help Menu Items	121

3.3.5.1 Help	122

3.3.5.2 Using Help	122

3.3.5.3 System Information	122

3.4 Communication Setting Method	123

3.4.1 Device	123

3.4.1.1 Serial	123

3.4.1.2 Network	125

3.4.1.3 Internal Computer Card	125

3.4.1.4 FieldBus, ProfiBus	125

3.4.1.5 OPC	125

3.4.2 Communication Settings	126

3.4.2.1 Device Settings	128

3.4.2.2 Protocol Settings	129

3.4.2.3 Dialup Settings	129

3.4.2.4 Line Duplex	130

3.4.2.5 Computer Duplex	130

3.4.2.6 Set Read Method	131

3.5 Communication Status Signal	132

Chapter4. Network Program	135

4.1 Network Memory Server / Client	135

4.1.1 Network Memory Server Settings	136

4.1.2 Network Memory Client Settings	138

4.2 Network Server / Client Configuration	139

4.3 Network Server	140

4.3.1 Running Network Server	140

4.3.2 Function Description for Each Text Menu	141

4.3.2.1 File Menu Item	141

4.3.2.2 View Menu Items	142

4.3.2.3 Config Items	146

4.3.2.4 Window Menu Item	149

4.3.2.5 Help Menu Item	149

4.4 Network Client	150

4.4.1 Running Network Client	150

4.4.2 Description for Each Text Menu	150

4.4.2.1 File Menu Items	151

4.4.2.2 View Menu Items	151

4.4.2.3 Config Menu Items	152

4.4.2.4 Windows Menu Items	154

4.4.2.5 Help Menu Items	154

Chapter5. SMS Manager	157

5.1 Running the SMS Manager	157

5.2 Whole Figure and Shortcuts Descriptions	158

5.2.1 Figure Descriptions	158

5.2.1.1 Program Name Display	158

5.2.1.2 Text Menu	158

5.2.1.3 Menu Button	158

5.2.1.4 Shortcut Button	158

5.2.1.5 Windows Internal Area	158

5.2.2 Shortcuts Descriptions	159

5.3 Description for Each Menu Item	160

5.3.1 File Menu Item	160

5.3.1.1 Send Manual Message	160

5.3.1.2 Send Test Message	161

5.3.1.3 SMS Message Queue	161

5.3.1.4 Exit	162

5.3.1.5 Open Windows Menu	162

5.3.2 View Menu Item	162

5.3.2.1 User Lists	162

5.3.2.2 Communication Code	164

5.3.2.3 SMS Sended Lists	165

5.3.2.4 Web Service State	166

5.3.2.5 Main Program	166

5.3.3 Config Menu Item	167

5.3.3.1 User Settings	167

5.3.3.2 Alarm Priority Settings	168

5.3.3.3 Message Format	168

5.3.3.4 Communication Port Settings	169

5.3.3.5 Settings	170

5.3.4 Windows Menu Item	171

5.3.5 Help Menu Item	171

Chapter 6. Line Printer Manager	173

6.1 Running Line Printer Manager	173

6.2 Whole Figure and Shortcuts Descriptions	174

6.3 Descriptions for Each Menu	175

6.3.1 File Menu	175

6.3.2 Config menu	175

6.3.2.1 Port Settings	175

6.3.2.2 Display Formats	176

6.3.2.3 Control Commands	176

6.3.3 Help Menu Items	177

Chapter 7. Watchdog	179

7.1 Run Watchdog	179

7.2 Whole Figure and Shortcuts Descriptions	180

7.3 Menu Bar Description	180

7.3.1 File Menu	180

7.3.2 View Menu	181

7.3.2.1 Log List	181

7.3.2.2 Hide	181

7.4 Shortcut Menus	182

7.4.1 Run Selected Programs	182

7.4.2 Modify Properties	182

Chapter 8. Running Server	185

8.1 Running Server	185

8.2 2 Whole Figure and Shortcuts Descriptions	186

8.3 Menu Bar Description	186

8.3.1 File Menu	186

8.3.2 View Menu	186

8.3.2.1 DB Integrations	187

8.3.2.2 Shared Server Status	188

8.3.3 Configuration Settings Menu	189

8.3.3.1 Database	189

8.3.3.2 Config Excel Path	194

8.3.3.3 Shared server	194

8.3.4 Help text menu	195

Chapter9. Configuration for Web server connection	197

9.1 System requirement	197

9.2 Installation of .NET Framework	198

9.3 Security settings	198

9.3.1 Registering as a trusted site	198

9.3.1.1 Adjust .NET Security	199

9.3.1.2 Register as a Trusted Site in Internet Explorer	202

9.3.2 Trust an assembly	204

<Empty Page>

<Empty Page>

# Chapter 1. General Outlines of Execution Program

AutoBase software, divided into two programs used for runtime and edit, works interactively with each program. (See <Figure 1-1> below).

<Figure 1- 1> Entire AutoBase Program Diagram

## 1.1 Types of Running Program

Execution programs are run interactively with Monitoring, Communication Server, Network Server / Client, SMS Manager, Line Printer Manager, Watchdog, Running Server, Web Server, etc.  (See <Figure 1-2> below.)

<Figure 1- 2> AutoBase Running Program Diagram

## 1.2 System Requirements

The following <Table 1-1> is required in order to set up AutoBase programs.

| SYSTEM | REQUIREMENTS |
| --- | --- |
| Mainframe | IBM-compatible PC, Pentium 4 or above |
| OS (Operating System) | Microsoft Windows 2000/XP/Server2003 or later |
| Main Memory Unit | 512M or above |
| Secondary Memory Unit | 200MB or above |
| Graphic Card | Windows Compatible |
| Keyboard | Windows Compatible |
| Mouse | Windows Compatible |
| Printer | Windows Compatible (If necessary) |
| Touch Screen | Windows Compatible (If necessary) |
| Others | Overlay Board, Camera, Digitizer, Plotter, etc. (If necessary) |

<Table 1- 1> AutoBase System Requirements

<Empty Page>

<Empty Page>

# Chapter 2. Monitor Program

Monitor Program, the AutoBase main program, is responsible for monitoring, controlling the field status, running script, collecting data, etc.

## 2.1 Run Monitor Program

Click on the ‘AutoBase’ () in the AutoBase Windows or the Start Program to run the monitor program.

<Figure 2- 1> AutoBase Windows Example

| 2.1.1 Using Startup Registering the monitor program or other required programs in the Startup makes the monitor program run whenever computers start up. The below <Figure 2-2> is the sample designed to immediately run the monitor program as soon as a computer boots by registering it in the Startup. | <Figure 2- 2> Example of a monitor program registered in Startup |
| --- | --- |

## 2.2 Whole Figure and Shortcuts Descriptions

### 2.2.1 Whole Figure Descriptions

The <Figure 2-3> below appears by running the monitor program.

<Figure 2- 3> Initial Screen Example of the Monitor Program

#### 2.2.1.1 Title Bar

Title Bars, the original feature of Windows, display program titles in the upper Windows as shown in <Figure 2-4>.

<Figure 2- 4> Example of Title Bar

#### 2.2.1.2 Menu Bar

The Menu bar contains File, View, Config Menu, etc.

You are able to select any menus by clicking on the left mouse button after moving the mouse to the Menu you want or using arrow and Enter key with holding ‘Alt’ or ‘F10’.

#### 2.2.1.3 Menu Button

The Menu Button shown with Text is located under the scroll bar moving left and right in monitor program.

The Menu Button might be not displayed according to the type of monitor screen and configuration.

#### 2.2.1.4 Windows Internal Area

Internal area of windows, indicating the context of monitor programs, is changeable depending on screen types and editing methods.

### 2.2.2 Shortcuts Descriptions

You can use the keyboard shortcuts listed below <Table 2-1>.

| SHORTCUTS | FUNCTIONS |
| --- | --- |
| ENTER | Select functions and check menus, etc. |
| ESC | Cancel functions and move back to previous the menu. |
| ,,, (arrow keys) | Move the internal Window up/down/ left/ right or between menus. |
| ALT, F10 | Move to the Menu Bar |
| CTRL+O | Log in users. |
| SHIFT+F5 | Cascade MDI Windows. |
| CTRL+F4 | Close the MDI Window currently selected. |
| Basic Shortcuts for Windows | Basic functions of Windows shortcuts |
| Others | Page Up, Page Down, Home and End Other function keys are available for various uses based on each monitor screen. |

<Table 2- 1> Shortcut Keys Descriptions for the monitor program

## 2.3 View Menu

Click on ‘View’ and you will see a drop down box as below <Figure 2-5>.

The menu consists of the following items:  Graphics, Entire tags, Analog inputs and outputs, Digital inputs and outputs, String tags, Registered groups, Alarm Files, Alarm Events, Log Files, Scripts, Communication Server, Reports, Demand Controls, Milli Datas, Schedules, DB Integrations and Navigation.

<Figure 2- 5> The Drop down box of View Menu

### 2.3.1 View Graphics

As a main feature of the monitor program, Graphics View screen can be differently configured depending on users and work fields.

Click on  on the Graphics screen and then the first screen ‘Startup.Modx’ appears and the screen returns to the previous graphics view with pressing .  Users are able to set in ‘Configuration Settings | Other Settings’ whether to display he Menu buttons below displayed on the bottom of the graphic screen.

The window of the Graphics consists of 2 types, Popup and MDI, installed in the Studio.

| When you click on the right mouse button providing help in the form of a menu of choices at the area neither having graphic elements nor responding to the mouse with graphic elements, the current graphics screen can be enlarged or reduced. Available to print out the Graphics screen currently being monitored when you choose ‘Print’ in <Figure 2-6>. The preview screen for graphics is run with pictures drawn in the Studio and users are able to refer to the editing program manuals or ‘Help’ for Studio usage. | <Figure 2- 6> Shortcuts on View Graphics |
| --- | --- |
| 2.3.1.1 Graphic Elements related to Analog |

When you move the mouse on graphic elements related to analog, a rectangle appears, once you click it, the menu is changed to the screen connected with analog set in Studio and details concerning selected analog tags are provided.

Additionally, pressing the right button, users are able to change the view menu to the shortcut menu <Figure 2-7>.

Only in case of setting the mouse response to graphic elements in Studio, the rectangle appears.

<Figure 2- 7> Shortcut Menus for graphic elements related to analog

1) Analog Rectangle

This graphic element indicates the rectangle size depending on the current value of analog tags as in the following <Figure 2-8>.  Therefore, the rectangle graphic element is made with length (the current minimum value) and breadth (the max) filled with the specified color from the bottom of the whole shape.

The rectangle graphic elements can select the bar direction such as top to bottom, bottom to top, left to right and right to left.

Available to set the rectangle size, color, location, analog input tags, mouse responses, bar direction of the graphic element for analog rectangles.

<Figure 2- 8> Method for Realizing the Feature of Analog Rectangle Graphic Element

(In case of top to bottom of the bar direction)

2) Analog Text

Analog text is a graphic element displaying the current value as follows <Figure 2-9>.

Possible to install font, font color, background color, tag titles, font size, display value, etc. in Studio.

You can choose display values in the current and integrated values.

<Figure 2- 9> The Example of the Graphic Element for Analog Text

3) Analog Meta

The current values are displayed with marked scales as follows <Figure 2-10>.

Analog tags, Meta size, etc. are set in Studio.

<Figure 2- 10> Example Analog Meta Graphic Element

The current value is displayed at a specific point of the fan shape between the maximum and the minimum.

The graphic element has a similar principle and shape with scales, pressure gauges, ammeters and voltmeters.

<Figure 2- 11> Method to display values of graphic elements for analog meta

4) Analog Status

Specific pictures, animations, etc. are indicated according to the current value of input tags.

The graphic elements are available to install the followings.

| (1) 0 bit, ON | (12) B bit, ON | (23) 6 bit, OFF | (34) High or above |
| --- | --- | --- | --- |
| (2) 1 bit, ON | (13) C bit, ON | (24) 7 bit, OFF | (35) Low or above |
| (3) 2 bit, ON | (14) D bit, ON | (25) 8 bit, OFF | (36) LoLo or above |
| (4) 3 bit, ON | (15) E bit, ON | (26) 9 bit, OFF | (37) HiHi or below |
| (5) 4 bit, ON | (16) F bit, ON | (27) A bit, OFF | (38) High or below |
| (6) 5 bit, ON | (17) 0 bit, OFF | (28) B bit, OFF | (39) Low or below |
| (7) 6 bit, ON | (18) 1 bit, OFF | (29) C bit, OFF | (40) LoLo or below |
| (8) 7 bit, ON | (19) 2 bit, OFF | (30) D bit, OFF | (41) Normal |
| (9) 8 bit, ON | (20) 3 bit, OFF | (31) E bit, OFF |  |
| (10) 9 bit, ON | (21) 4 bit, OFF | (32) F bit, OFF |  |
| (11) A bit, ON | (22) 5 bit, OFF | (33) HiHi or above |  |

Graphic elements for the analog status are indicated in the monitor program as one of the following 5 pictures with setting.

If the graphic elements are set such as <Figure 2-12> in Studio, one of the following 5 pictures appears in the monitor program.

(1) Current values are HiHi or above, Red

(2) Current values are High or above, Yellow

(3) Current values are Low or below, Green

(4) Current values are LoLo or below, Blue

(5) Excluding 4 cases, White

<Figure 2- 12> The example of setting graphic elements for analog status

5) Analog Rotation

This graphic element displays current analog values using the image rotation angles.

The analog input tags, rotate images, angles and directions, background and background color, whether to respond to the mouse, etc. are set in Studio.

Rotate images used in graphic elements contains two images : default and specific images created by users. For more information how to make rotating images, refer to the user manual for the edit program.

The following <Figure 2-13> is an example of analog rotation graphic element and <Figure 2-14> shows how to display it.

<Figure 2- 13> Example of Analog Rotation Graphic Element

<Figure 2- 14> Method to Display Analog Rotation Graphic Element

#### 2.3.1.2 Graphic Elements related to Digital

The graphic elements connected with digital display animations or bit-map pictures depending on the status ‘ON’ and ‘OFF’ of digital tags including digital animation, circles, rectangles and text.

<Figure 2- 15> Example of Graphic Elements related to Digital

When users place the mouse pointer over the graphic element relevant to digital, the rectangle appears around it as <Figure 2-15>.  Click the left mouse button there, and then the menu displays detailed information of selected digital tags with the related digital screen set in Studio.

| Additionally, if you press the right mouse button on the rectangle image, the shortcut menu appears such as <Figure 2-17>. Unless you install the mouse response in Studio, no rectangles are displayed despite the mouse point over the graphic element. The following <Figure 2-16> is the dialog box to confirm output operations appearing in case of choosing to change digital input values. <Figure 2- 16> Example of the dialog box for changing digital input values | <Figure 2- 17> Shortcut Menu for Graphic Elements Related to Digital |
| --- | --- |

1) Digital Animation

<Figure 2-18>, the graphic element, helps users simply verify input values on graphic screen by setting pictures or animation in the event that the digital current values are ON or Off.

<Figure 2- 18> Example of Graphic Elements for Digital Animation

The status of digital input tag when digital animation is set such as <Figure 2-18>, ‘ON’ of input tag status is shown with the image () or animations and ‘OFF’ is displayed with .

Users set digital tags, types of pictures or animation, pictures’ location, etc. in Studio.

<Figure 2-19> showing how to display animations is an animation file created with several images shown alternately at regular intervals (1/18 sec) which looks like a moving image on screen.

<Figure 2- 19> How to Display Animations

※ Refer to the Editing Program Manual to make animation files.

2) Digital Circle

The following graphic screen indicates the circle size, color, etc. set in Studio depending on the status of digital input tags.  <Figure 2-20> is an example of graphic elements for digital circles.

<Figure 2- 20> Example of graphic element for digital circles

3) Digital Rectangle

This graphic element shows the rectangle size and color set in Studio, and the following <Figure 2-21> is an example of digital rectangle elements on screen.

<Figure 2- 21> Example of graphic elements for Digital Rectangles

4) Digital Text

The graphic element of ‘Digital Text’ shows the current values as texts in the followings <Figure 2-22> and the font size and color, font, element locations, digital input tags, etc. are set in Studio.  The text is displayed specified with less than 6 characters (refer to the tag settings) such as ‘ON’, ‘OFF’ or ‘START’, ‘STOP’, etc. in the digital tag property.

<Figure 2- 22> Example of graphic elements for Digital Texts

#### 2.3.1.3 Graphic Element related to button

Graphic elements connected with buttons made up of 4 types such as module selection and hide, script execution and digital print buttons makes it possible to change monitor screen to the installed image module and to implement script, digital group print, etc.

Graphic elements displaying little squares with the mouse on buttons.

When using module hide buttons, the square graphic element appearing with putting your mouse on buttons indicate that the buttons are selected and the monitor screen is moved to the image module by clicking on the left mouse button.  Except for these buttons, you can run functions or specified contents by clicking on the left mouse button on buttons.

1) Module Selection Button

Several images are used when it is hard to show the entire process with an image to supervise the field by means of changing graphic screens, and users can move them by clicking buttons of module selection and hide and script execution.

Module Selection Buttons displayed like <Figure 2-23> are available to modify the graphic monitor screen to the set image module.

<Figure 2- 23> Module Selection Button Example

2) Module Hide Button

Module Hide Buttons having the same feature of Module Selection Buttons are not shown on graphic monitor screen and when users position the mouse on them set in Studio, rectangles are displayed indicating that the module is selected.

<Figure 2-24> is an example showing a selection of Module Hide Buttons.

<Figure 2- 24> A screen example with a selection of Module Hide Buttons

3) Script Button

This is to execute the run program or other scripts by displaying buttons on the graphic display as shown <Figure 2-25>.  You can set the size, color, location of the button and the text on it in Studio.

<Figure 2- 25> Script Button Example

4) Digital Output Button

Digital output is available on the tag set in Studio making it possible to set the size, color, location, fonts on button, etc. of the digital output button.

<Figure 2- 26> Digital Output Button Example

When you press digital output buttons (See the <figure 2-26>), the dialog box <Figure 2-27> to check digital output appears.

The number of digital output tags available to be set with the digital output buttons is 1 ~ 32767.

<Figure 2- 27> Dialog Box to Check Digital Output Button

#### 2.3.1.4 String Tag

String Tag display assigned strings on graphic monitor screen.  Users are able to set string tag titles, font and background color, whether to respond to the mouse, etc. in Studio.

Possible to change sentences which are going to be displayed in a dialog box manually as the following <Figure 2-28> after setting string tag graphic elements to respond to the mouse and selecting it.

<Figure 2- 28> Dialog box example for strings change

#### 2.3.1.5 Graphic Module

The graphic element for graphic module is used to monitor several graphic screens on one using created module files as graphic elements.

<Figure 2-29> is an example for graphic monitor screen configured with 5 graphic elements and module selection buttons.

<Figure 2- 29> Example of Monitor Screen Configured with Graphic Module Element.

#### 2.3.1.6 Alarm Window

Alarm window display on monitor screen specific types of alarms available to be set by selecting ‘During alarms’ or ‘Until users confirm’ on ‘Alarm Priority’ Menu, Studio.

Studio is in charge of setting original titles of alarm window, text size to be displayed, method for arranging alarms, etc.

<Figure 2- 30> of Monitor Screen Configured with Graphic Module Element

| <Figure 2-30> is a monitor screen example with alarm window and running script for alarm messages, and <Figure 2-31> is a shortcut menu (mouse right button). In order to confirm or cancel alarm messages indicated on alarm windows, either select menu such as alarm confirmation, etc. on <Figure 2-31> or write a script related to alarms (such as AlarmListConfirm, etc. ). | <Figure 2- 31> Alarm Window Shorten Menu |
| --- | --- |

#### 2.3.1.7 Multi-graph

Multi-graph show the changes of analog and digital current values for specified times with graphs as the followings <Figure 2-32>.

Analog and digital tags, line color and styles, indicated values, data range, text and its color, class titles, view boundaries, collection cycles, etc. are set in Studio.

Users can install whether set tags are displayed on multi-graph screen or not, if press the left mouse button on a tag property display of graphic elements for multi-graph.

Additionally, available to make sure the maximum, minimum and average values in the changed range, when move the mouse with pressing the left mouse on graph data display.

<Figure 2- 32> Example Showing Monitor Screen Configured with Graphic Elements for Multi-graph

#### 2.3.1.8 Multi-trend

The multi-trend displays the changes of analog input values (the average, maximum, minimum, integrated, difference values, etc.) or digital operation status for specific minutes, hours, days and months.

<Figure 2- 33> Example Displaying Monitor Screen Configured with Graphic Elements for Multi-trend

Users are able to set analog and digital tags, line color and styles, indicated values, time range, text and its color, graph names, etc. for multi-trend in Studio.

The Settings dialog box such as <Figure 2-34> available to install trend length, graph start time, etc. appears if click the left mouse button outside the data display of graphic elements for multi-trend.

Moreover, if press the right mouse button and move the mouse, time for data moves as much as the extent the mouse does, and also possible to see the maximum, minimum and average values in the changed range, once move the mouse with pressing the left mouse.

<Figure 2- 34> Multi-trend Setting Dialog Box in Monitor Program

After checking ‘Use local ranges’ in the settings dialog box <Figure 2-34>, if you click the right mouse button inside multi-trend maximum and minimum values display area, the dialog box <Figure 2-35> able to regulate the multi-trend graph range comes up.

<Figure 2- 35> Graph Range Setting Dialog Box Example

Press the left mouse button on each multi-tag name, maximum, minimum, current and data value area, you can check whether the selected tags are displayed or not, and change them to the standard tags with clicking the right mouse button.

#### 2.3.1.9 Demand Window

Demand Window, one of graphic elements, to indicate the demand controls status as graph is usually used to analyze flow and a quantity of electric power for 15 minutes.

Tags used for power input, estimated power display, target power, cutoff and control and control time, text, background color, etc. is set in Studio. The following <Figure 2-36> is an example of graphic elements for demand window and <Figure 2-37> is about Display Principle for Demand Window.

<Figure 2- 36> Example of Graphic Elements for Demand Window

<Figure 2- 37> Display Principle of Graphic Elements for Demand Window

#### 2.3.1.10 Milli-Data Window

The milli-data window collects the set analog and digital tag at intervals of 1 to 60,000 msec and displays such as the following <Figure 2-38> using MDB data format.

The upper window of milli-data windows shows all gathered data, and the lower one indicates the data values selected on the upper.

Users make it possible to select area to display on the lower window by pressing and holding the left mouse button, then moving it.

Available to set data tag, data intervals, collection conditions, display text and it color, etc. in Studio.  Also, users are able to choose display data and install the display method of time axis for micro data window with writing script such as MilliDataSetFile and MilliDataSetTimeType in Studio.

<Figure 2- 38> Example of Graphic Elements for Milli-Data Window

#### 2.3.1.11 Graphic Element related to Window Control.

Window Control used for windows such as List Box, Combo Box, Edit Box, Radio Button and Check Box is a component to configure graphic monitor screen.

| 1) List Box This is to display lists such as <Figure 2-39> on graphic screen and data, related tags, text, display format, etc. are set in Studio. | <Figure 2- 39> Example of Graphic Element for List Box |
| --- | --- |
| 2) Combo Box This is to show combo box like <Figure 2-40> on Graphic Screen and Studio is responsible for setting data, relevant tags, text, display format, etc. | <Figure 2- 40> Example of Graphic Elements for Combo Box |
| 3) Edit Box This is to indicate Edit Box as an example <Figure 2-41> and available to install connected tags, text, etc. in Studio. | <Figure 2- 41> Example of Graphic Elements for Edit Box |
| 4) Radio Button This is to display radio buttons such as <Figure 2-42> and item data, relevant tags, text and it color, etc. are set in Studio. | <Figure 2- 42> Example of Graphic Element for Radio Button |
| 5) Check Box This shows check boxes on Graphic Screen and tags, display contents, text and its color, etc. installed in Studio. | <Figure 2- 43> Example of Graphic Elements for Check Box |

#### 2.3.1.12 Database

Database displays database data for example Access (MDB format), SQL Server, Oracle, etc. as the same format of <Figure 2-44>.

Database types, text and its color, etc. are set in Studio.

<Figure 2- 44> Example of Graphic Elements for Database

The following <Figure 2-45>, a setting dialog box for a database element available to install column names, display text, start point and whether, display or not, etc.  You are able to select it by clicking the right mouse button on the database element.

<Figure 2- 45> Example of Dialog Box for Database Column

#### 2.3.1.13 Real-time Test Graph

Real-time test graph is to display the change of specific tag values for set time with graph.

The graph with dots on the following <Figure 2-46> indicates standard tag values.

<Figure 2- 46> Example of real-time test graph

The base tag is used to check out how close the actual values are to the standard one by inputting changing values such as temperature, pressure and so on when running.  You can set the base and actual tag, color and font of the real-time graph in Studio.

#### 2.3.1.14 XY Graph

This XY Graph is to see the changes of current values for a couple of tags for set time as the followings <Figure 2-47>.

<Figure 2- 47> Example of XY Graph

The view range is 1 to 10,000, and data collection intervals are 1 to 60,000 msec.

Studio is responsible for the number of components, collection intervals, graph components, font and is color, etc.

#### 2.3.1.15 Database Trend

This displays data stored with time in database such as <Figure 2-48> using trend format, graphic element. User are able to install database types, table names, data time format, column, analog and digital tags connected with column, line color and styles, display values, time range, font and it color, graph names, etc. in Studio.

<Figure 2- 48> Example of monitor screen with the graphic element for database

Click on the left mouse button outside of display of graphic elements on monitor screen, the settings dialog box such as <Figure 2-49> appears.

<Figure 2- 49> Settings Dialog Box of Database Trend on Monitor Program

Press the right mouse button on display area showing the maximum and minimum for database trend and then you can control the graph ranges after checking ‘Use local ranges’ on <Figure 2-49>.

Additionally, users can decide whether selected tags are displayed or not if push the left mouse button on tag names, maximum, minimum, current values and data values for each database trend as well as alter the chosen tags to standard ones with clicking on the right mouse button.

#### 2.3.1.16 Display Changes

‘Display Changes’ is a graphic element to indicate the current analog input values and the tags changed with digital input status.

Users are able to set the list numbers (1~100) of graphic elements to display changes, font and background colors, fonts, class names, extensions, etc.

#### 2.3.1.17 Bitmap

This graphic element showing bitmap images commonly use smaller images than background ones.

<Figure 2-50> is an example of graphic screen by inserting bitmap image files on the background.

Users are able to connect pictures to tags using extensions or make them move, reduce, enlarge, etc.

<Figure 2- 50> Example displaying graphic elements inserted on background picture

#### 2.3.1.18 Animation

This element is to show animated pictures on graphic screen. Animation types and locations are specified in Studio.

The upper picture of <Figure 2-51> is that animation elements are inserted on graphic monitor screen, and the lower is to display one of the animated picture files.

<Figure 2- 51> Example of Inserted Animation

That is, the upper picture looks like it actually moves by showing 5 images on the lower screen in rotation at regular intervals. (Setting in animation editors or extension scripts)  You are able to connect animation to tags or operate it for animation speed, movement, reduction, enlargement, etc. using extensions.

#### 2.3.1.19 Single line text

Text is indicated on graphic screen as the followings <Figure 2-52>, and font types, size, color, location, etc. are set in Studio.

Text elements consist of ‘Single line text’ and ‘text’, and text size, style, location, etc. can be changed using extension.

<Figure 2- 52> Example of a Text Element

#### 2.3.1.20 Rectangle

This element is to show rectangle and button shapes on graphic screen, and Studio is responsible for setting rectangle size, stroke thickness, shapes (rectangles or buttons), locations, extensions, etc.

The following <Figure 2-53> is an example of rectangle elements based on setting.

<Figure 2- 53> Example of rectangle elements depending on setting

#### 2.3.1.21 Circle

Circles are displayed on graphic screen such as <Figure 2-54>, and the size, stroke thickness, location, extension, etc. are installed in Studio.  This element can connected to tags, or operated for animation speed, movement, reduction, enlargement, etc. using extensions.

<Figure 2- 54> Example of Circle element based on setting

#### 2.3.1.22 Line

<Figure 2-55> is an example to indicate lines on graphic screen and the line length, thickness, locations, extensions, etc. are set in Studio.

It is possible to connect to tags or move, reduce, enlarge the graphic elements using extensions.

<Figure 2- 55> Graphic Element Example of the Line Based On Setting

#### 2.3.1.23 Polygon

<Figure 2-56> below is to show polygon elements and the shapes, size, locations, stroke thickness, extensions, etc. are installed in Studio.

Moving, reducing, and enlarging the graphic element representing polygons are available.

<Figure 2- 56> Graphic Element Example of the Polygon Based On Setting

#### 2.3.1.24 Rounded Rectangle

Rectangles with Rounded Corners which has same features with normal rectangles except for outer forms can be displayed on graphic screen with setting the shapes, size, locations, stroke thickness, extensions, etc. in Studio.

#### 2.3.1.25 Curve

This element indicate curves and the shape, size, locations, line thickness, extensions are set in Studio.

#### 2.3.1.26 Clock

Clock elements show the current time including analog and digital display forms such as <Figure 2-57> on graphic screen, and also users can customize the locations, size and color in Studio.

<Figure 2- 57> Graphic Element Example of the Clock

#### 2.3.1.27 Date

This graphic element indicates the current date, and the location, size, color, etc. are set in Studio.  The following <Figure 2-58> is an example of showing dates and has several options to select, for instance ‘disable the display of days’, ‘Korean or English’, ‘year/month/day or year/month/day’ for date display.

<Figure 2- 58> Graphic Element Example of Date

#### 2.3.1.28 Background Bitmap

Bitmap images are used for the background of graphic module screen, and uses are able to install background ones in Studio.

#### 2.3.1.29 Background Color

Picture areas except for buttons, analog or digital graphic elements, background pictures, etc. are filled with background color set in Studio.

#### 2.3.1.30 Group

The group is made as a graphic element by putting analog or digital graphic elements, rectangles, circles, straight line, etc. together. It is available in only Studio, and graphic elements runs independently in graphic monitor.

#### 2.3.1.31 Extension of Graphic Element

Most graphic elements have extension such as size, mouse responses, view, color, etc. available by writing script.  For more details on how to write scripts for the extensions, refer to the instruction of the editing program.

### 2.3.2 Entire Tags

<Figure 2- 59> Example of View Screen for Entire Tags

View screen for all tags such as <Figure 2-59> appear with selecting ‘View | Entire tags’ in text menu.

Entire tags view is able to monitor or control all tag values and setting status for example analog input and output, digital input and output, strings and group tags, etc.

As an example of <Figure 2-59> above, on the left side of entire tags view displays trees for group, and the right is for tag names belonging to each group, explanation, current values, setting status, etc.

| After selecting the first tree (Local) of entire tags view, press the right mouse button, and then a shortcut menu such as <Figure 5-60> appears. A setting dialog box comes up by choosing ‘Tags View Settings’. | <Figure 2- 60> First Tree Shortcut Menu of Entire tags view |
| --- | --- |

<Figure 2- 61> Dialog Box to Set ‘Tags View Settings’

| Tags for all groups are displayed on the first tree with checking ‘Display all tags on the root tree’ in the <Figure 2-61>. Press the right mouse button on the right tag list of all tag view, and then available to run shortcut menu as indicated <Figure 2-62> or a detailed monitor, settings, etc. with the menu button on the bottom of the screen. If double-click the left mouse button on the tag list, it is moved to a detailed monitor screen for each tag. Able to move to a detailed monitor screen with selecting ‘Detail View’ on the short menu for all tag view list or on the menu button. Group tag is transferred to the screen to select the subgroup, and string tags open the dialog box available to modify tag properties. Select ‘analog input’, ‘analog output’, ‘digital input’, ‘digital output’, ‘string tag’ on the shortcut menu of all tag view list, and then possible to choose tag monitor screen for each tag of Chapter 2.3.3 ~ 2.3.7. Other shortcut menus and menu buttons for all tag view have the same way of using shortcut menus and buttons for analog, digital, and string monitor screen. | <Figure 2- 62> Shortcut menu for all tag view list |
| --- | --- |

### 2.3.3 Analog Inputs

When you select ‘View | Analog Inputs’ in text menu, the analog input view screen as followed <Figure 2-63> appears which displays tags, explanation, current values, setting status. etc. and modifies tag contents.

Double click  from the menu, ‘Analog Input Detail’ from the shortcut menu, or the left mouse button of the selected tags, available to move to Detail View of analog input.

For more details about the Detail View, refer to chapter 2.3.3.1.

Analog Trend Diagnosis Screen comes up if choose  from Menu or ‘Analog Trend Diagnosis’ from the shortcut menu, and details concerning this are explained in chapter 2.3.3.2.

<Figure 2- 63> Example of Analog Inputs View

The screen is moved to analog data view by clicking  from menu or Analog Data View from shortcut menu.

Refer to the chapter 2.3.3.3 for more information about analog data view.

, ,  from menu are to set whether to use alarms, data and tags for selected analog input tag.

| A shortcut menu appears (see <Figure 2-64>) when you click the right mouse button on the selected list of analog input view. | <Figure 2- 64> Shortcut Menu of ‘View Analog Input’ |
| --- | --- |

The properties of Analog input tag can be changed in the dialog box such as <Figure 2-65> by selecting  from menu or ‘Tag Properties’ from shortcut menu.

<Figure 2- 65> Dialog Box to Tag Properties of Analog Input Tag

Users are able to set alarm levels of analog input tags such as HiHi, High, Low, LoLo in the dialog box as followed <Figure 2-66> with selecting  from Menu.

<Figure 2- 66> Dialog Box for Analog Alarm Level Settings

Analog set points are able to be changed in the dialog box such as <Figure 2-67> by choosing ‘Change &Value’ from the shortcut menu for Analog Input View. The tag property set with either memory tags or AO and SV factors is required to change analog set points.

<Figure 2- 67> Dialog Box to Change Analog Set Points

For manual input settings, click on ‘Set Temporary Value’ functioning the current values of specific tags to fix random values.

<Figure 2- 68> Example of Dialog Box for Analog Temporary Value

Users can find tags what they want, when inputting tag names or sequence numbers to find in the dialog box <Figure 2-69> by selecting ‘Tag Search’ from the shortcut menu.

Color of background, text, tag, explanation and font, font size, etc. are available to be set by choosing Text Menu from Configuration.

<Figure 2- 69> Dialog Box to Find Tags Using Tag Name or Position

#### 2.3.3.1 Analog Input Details

<Figure 2- 70> Detail View Example of Analog Input

Analog input details possible to be moved from graphic elements and scripts connected with View of Analog Input, Entire Tags, Registered Groups, etc. show real- time trend diagnosis for analog input values and set points as above <Figure 2-70>.

| Simply clicking the right mouse button on Detail View can bring up a shortcut menu such as <Figure 2-71>. | <Figure 2- 71> Shortcut Menu of Detailed View Screen of Analog |
| --- | --- |

Select  from the menu bar or ‘View Settings’ in the shortcut menu, the dialog box for detail view settings as below <Figure 2-72> appears.

<Figure 2- 72> Example of Dialog Box to set Analog Input Detailed View

To move to the analog trend diagnosis screen, click on , , , , ,  from menu buttons or ‘Analog Trend for 1 Hour ~ Analog Trend for 30 Days’ in the shortcut menu. Chapter 2.3.3.2 will explain analog trend diagnosis.

Analog Data View will open by pressing ‘Analog Minutely Data ~ Analog Monthly Data’. For more details, refer to chapter 2.3.3.3.

Users can change the set points using ‘Change Value’ and tag properties by selecting ‘Tag Properties’.

It is possible to fix analog current values as random values when click on ‘Set Temporary Value’ in the shortcut menu, and also to display details about previous and next tag using Page Up or Page Down keys on Analog Detail View Screen.

Background and text color, font and its size, etc. are set in Font or Color from Text Menu in the configuration menu.

#### 2.3.3.2 Analog Trend Diagnosis

This trend diagnosis for 1, 8, 24, 48 hours and 30 days shows the flow of input values such as <Figure 2-73> using saved minute data.

<Figure 2- 73> Example of Analog Trend Diagnosis.

| This screen can be transferred from Analog Inputs, Entier Tags and Registered Groups, Analog Details and Data View, graphic elements and scripts relating to Analog, etc. Press the right mouse button on the Analog Trend Diagnosis Screen, and then the shortcut menu <Figure 2-74> comes up. The trend diagnosis data can be displayed with the order such as average → minimum → maximum → integration → total by pressing from the menu button. | <Figure 2- 74> Shortcut Menu for Analog Trend Diagnosis Screen |
| --- | --- |

Settings for Max / Min in Trend Diagnosis, Data Reading Interval, View Method, Start Time for Data View, etc. is available in a dialog box for Analog Trend Diagnosis Settings as below <Figure 2-75> by choosing Settings one of  and  from menu buttons or ‘View Settings’ in the shortcut menu.

<Figure 2- 75> Dialog Box to Set Analog Trend Diagnosis

Selecting Time Change  from menu buttons is possible to change Start Time for Data View. You are able to confirm current values by selecting either  or  and to increase or decrease the Start Time for Data View by 1/8/24/48/72 hour or 30 day in case of clicking on , ,  or .

Moreover, choosing ‘Analog Trend for 1 Hour ~ 30 Days’ can make trend diagnosis time change.

Analog Data View appears after selecting ‘Analog Minutely Data ~ Analog Monthly Data’ and you will look at the details in chapter 2.3.3.3.

Analog set points and tag property can be changed using ‘Change Value’ or ‘Tag Properties’.

‘Set Temporary Value’ features to fix current values for specific tags as random values.

Pressing Page Up or Page Down displays previous or next tag for analog input on the trend diagnosis screen. The background and text color, font and the size, etc. are installed in Font or Color from text menu in configuration menu.

Multi Trend Diagnosis showing several analog tags using script functions, etc. comes up when writing scripts below in script run button from Studio.

@MultiRegister("PTE_AHU1", 127, 2);

@MultiRegister("PTE_AHU2", @RGB(0, 127, 0), 1);

@MultiRegister("PHE_AHU1", 0, 3);

@SetBackColor(@RGB(255, 255, 255));

@MultiTrend(1);

Explanations : The monitor screen opens about analog trend diagnosis for 1 hour (3 diagnosis at the same time) with 3 tags for PTE_AHU1, PTE_AHU2, PHE_AHU1 and white background. (Refer to the edit program manual)

#### 2.3.3.3 Analog Data View

Analog Data View using numbers of graphs to indicate data for each minute, hour, day, week and month as below <Figure 2-76> can be moved from Analog Inputs, Entire Tags, Registered Groups, analog details and trend diagnosis, graphic elements and script connected with analog.

<Figure 2- 76> Example of Analog Data View Screen

| When you click on the right mouse button on analog data view, the shortcut menu such as <Figure 2-77> appears. Choosing is available to show trend diagnosis data with the changed order such as average → minimum → maximum → integration → total. Users are able to modify settings for maximum and minimum in Trend Diagnosis, view type, display time in graph, integrated value, etc. in the dialog box such as <Figure 2-78>, if click on from the menu buttons or ‘View Settings’ in the shortcut menu. | <Figure 2- 77> Shortcut Menu to View Analog Data |
| --- | --- |

<Figure 2- 78> Example of Dialog Box for Analog Data View Settings

Data view with the order (minutely → hourly → daily → weekly → monthly) can be displayed when selecting  from menu buttons.

Users can change analog data view display method into the sequence (numbers → line graph → bar graph) when selecting  from menu buttons.

Choosing  can make Start Time for Data View change, and also the time is increased or decrease using  and .

Analog Trend Diagnosis comes up by pressing one of ‘Analog Trend for 1 hour ~ 30 Days’ and refer to chapter 2.3.3.2 for more details.

Analog data view time is modified by clicking on ‘Analog Minutely Data ~ Monthly Data’.

Users can change the set points using ‘Change Value’ and tag properties by selecting ‘Tag Properties’.

Clicking on ‘Set Temporary Value’ from the shortcut menu can make the current value fix as random values.

Clicking on Page Up or Page Down displays previous or next tag for analog input on the analog data view screen.

The background and text color, font and the size, etc. are set in Font or Color from text menu in configuration menu.

Analog multi data view displaying data concerning several tags using script functions, etc. is written as below.

@MultiRegister("PTE_AHU1", 127, 0);

@MultiRegister("PTE_AHU2", @RGB(0, 127, 0), 1);

@MultiRegister("PHE_AHU1", 0, 3);

@MultiRegister("PHE_AHU2", @RGB(127, 127, 0), 5);

@SetBackColor(@RGB(255, 255, 255));

@MultiData(0, 2);

Explanations : Data view with 4 line graphs are run at the same time along with 4 tags such as PTE_AHU1, PTE_AHU2, PHE_AHU1, PHE_AHU2 and white background. (Refer to the edit program manual)

### 2.3.4 Analog Outputs

Select ‘View | Analog Outputs’ from the Text Menu, and then the analog output view (See <Figure 2-79>) appears.

<Figure 2- 79> Example of Analog Outputs View

| Analog Output View is the screen available to display all tag names for output tag, tag explanations, current values, setting status, etc. and modify tag contents. |
| --- |
| Double click on the right mouse button on the selected list from analog output view screen to view the shortcut menu such as <Figure 2-80>. Screens move to the Analog Output Detail View by pressing or double clicking on ‘Analog Output Detail’ from shortcut menu. For more details, refer to chapter 2.3.4.1. | <Figure 2- 80> Shortcut Menu for Analog Output View |

By choosing  buttons or ‘Change Value’ from the shortcut menu, it makes it possible to output setting values for analog output tag in the dialog box as below <Figure 2-81>.

The button  from menu is to install whether to use selected tag or not.

Clicking on the button  or ‘Tag Properties’ makes it possible to change properties for analog output tags in the dialog box as following <Figure 2-82>.

<Figure 2- 81> Dialog Box to Change Analog Output Values

<Figure 2- 82> Dialog Box to Change the Tag Property of the Analog Output

#### 2.3.4.1 Analog Output Details

Analog Output Details indicating real- time trend diagnosis and set points for analog output current values as below <Figure 2-83> can be moved from Analog Outputs, Entire Tags, Registered Groups, scripts, etc.

<Figure 2- 83> Example for Analog Output Details

| By clicking on the right side button on a mouse, the shortcut menu <Figure 2-84> comes up. Selecting button from the Menu or ‘Change Value’ in the shortcut menu can make points installed for analog output tag in the dialog box <Figure 2-81> output. | <Figure 2- 84> Shortcut Menu for Analog Output Detail View |
| --- | --- |

Tag properties are changeable in case of choosing ‘Tag Properties’ button.

The Detail View Screen of previous and next tag for analog output opens using Page Up or Page Down on Analog Output Detail View Screen.

Background and text color, font and its size, etc. on the output detail view screen are installed in Font or Color buttons from Text Menu of Configuration.

### 2.3.5 Digital Inputs

To display Digital Inputs View screen as below <Figure 2-85> indicating tags explanations, current values, settings status, etc. for all digital input tags, select ‘View | Digital Inputs’ from the Text Menu.

<Figure 2- 85> Digital Inputs View

| Press the right side button on a mouse on the selected list from Digital Inputs View, the shortcut menu <Figure 2-86> appears. To move to Digital Input Detail View, choose , or double click on the left side of a mouse in the selected tag. For more information for use, refer to chapter 2.3.5.1. Digital input values in the dialog box (See <Figure 2-87>) are changeable via or ‘Change Value’ buttons requiring memory tags for properties or Out1, Out2 set. | <Figure 2- 86> Shortcut Menu for the View Screen of Digital Input |
| --- | --- |
| Digital Trend Diagnosis is displayed when select button or one of ‘Digital Trend for 1 Hour ~ 30 Days’, and chapter 2.3.5.2 includes more explanations. The way to show digital data view is clicking or one of ‘Digital Minutely Data ~ Monthly Data’ and more details are in chapter 2.3.5.3. | <Figure 2- 87> Example of Dialog Box for Digital Input Value Change |

, ,  from menu are to set whether to use alarms, data and tags for selected digital input tag.

Users are able to change the property for digital input tag in <Figure 2-88> using ‘Tag Properties’ or  from the menu buttons.

<Figure 2- 88> Example of Dialog Box for Digital Input Tag Property Change

Current values of Digital Input Tags can be settled as random values when selecting ‘Set Temporary Value’ in <Figure 2-89>.

<Figure 2- 89> Example of Dialog Box for Manual Digital Input

Inputting tag names or sequence numbers with choosing ‘Tag Search’ make users possible to find tags that they want.

Users can install color of background, text, tag, explanation and font, its size, etc. in Font and Color from Configuration Menu.

#### 2.3.5.1 Digital Input Details

<Figure 2- 90> Example of Digital Input Details View

| Digital Input Details display real–time trend diagnosis of current values for digital input and set points, etc. as below <Figure 2-90> and can be moved from View Screen for digital input, entire tag, registered group as well as graphic elements and scripts relating to digital. Shortcut Menu such as <Figure 2-91> comes up by clicking on the right mouse button on this screen and <Figure 2-92> appears using or ‘View Settings’. | <Figure 2- 91> Shortcut Menu for the Detailed View Screen of Digital |
| --- | --- |

<Figure 2- 92> Dialog Box to Set the Detailed View of Digital Input

The current values for digital input can be changed with choosing  or ‘Change Value’.

Screens move to the Digital Trend Diagnosis when pressing one of , , , , ,  or ‘Digital Trend for 1 Hour’ ~ ‘or 30 Days’ from the shortcut menu. Chapter 2.3.5.2 has more details.

Digital Data View is moved by clicking on ‘Digital Minutely Data’ ~ ‘Digital Monthly Data View’ on the shortcut menu and chapter 2.3.5.3 includes details.

Tag properties are changeable in case of choosing ‘Tag Propertites’ Change button.

Clicking on ‘Set Temporary Value’ from the shortcut menu can make the current value fix as random values. Hitting Page Up or Page Down displays previous and next tag for digital input on Digital Data View.

The background color, font, font color and size, etc. of the detailed view screen are set in Font and Color from sub menus in Configuration Menu.

#### 2.3.5.2 Digital Trend Diagnosis

This displays the flow of digital input values such as <Figure 2-93> using saved minute data and includes several screens for example 1, 8, 24, 48 , 72 hours and 30 days trend diagnosis available to be moved from View Screen for digital input, entire tag, registered group as well as graphic elements and scripts relating to digital.

<Figure 2- 93> Example of Digital Trend Diagnosis

| The shortcut menu <Figure 2-94> comes up by clicking on the right side of the mouse on the screen. | <Figure 2- 94> Shortcut Menu of Digital Trend Screen |
| --- | --- |

Setting up data reading interval, data view, trend diagnosis start time, etc. is available in the dialog box <Figure 2-95> using , Data Intervals:1min from menu buttons or ‘View Settings’ from the shortcut menu.

<Figure 2- 95> Example of Dialog Box for Digital Trend Settings

Choosing  can change data view start time.

Users are able to check current values out by selecting ,  and change data view start time using , ,  or  from the menu buttons.

Time for Digital Trend Diagnosis View is possible to be changed by pressing one of ‘Digital Trend for 1 Hour ~ Digital Trend for 30 Days’.

Digital Data View is moved by clicking on ‘Digital Minutely Data ~ Digital Monthly Data’ on the shortcut menu and chapter 2.3.5.3 includes details.

The current values for digital input can be changed with choosing ‘Change Value’.

Tag properties are changeable in case of choosing ‘Tag Properties’ Change button.

Clicking on ‘Set Temporary Value’ from the shortcut menu can make the current value fix as random values.

Hitting Page Up or Page Down displays previous and next tag for digital input on Digital Data View.

You can set the background color, font, font color and size, etc. of the digital trend screen from submenus of the Configuration Menu.

#### 2.3.5.3 Digital Data View

<Figure 2- 96> Example of Digital Data View

| Digital Data View displaying minutely, daily, weekly and monthly data using status values such as ON/OFF can be moved from View screen for Digital Inputs, Entire Tags, Registered Groups and digital input details, trend diagnosis, graphic element relating to digital, scripts, etc. <Figure 2-97> comes up by clicking on the right mouse button on the screen. | <Figure 2- 97> Shortcut Menu for Digital Data View |
| --- | --- |

Users are able to change the order for Analog Data View (minutely → hourly → daily → weekly → monthly) by choosing  from menu buttons.

Choosing  can make Start Time for Data View change, and also the time is increased or decrease using  and .

Digital Trend Diagnosis comes up by pressing one of ‘Digital Trend for 1 Hour ~ Digital Trend 30 Days’ and chapter 2.3.5.2 includes more details.

Digital data view time is modified by clicking one of ‘Digital Minutely Data ~ Digital Monthly Data’ from the shortcut buttons.

The current values for digital input can be changed with choosing ‘Change Value’.

Tag properties are changeable in case of choosing ‘Tag Properties’ button.

Clicking on ‘Set Temporary Value’ from the shortcut menu can make the current value fix as random values.

Hitting Page Up or Page Down displays previous and next tag for digital input on Digital Data View.

Background and text color, font and its size, etc. are set in Font or Color from Text Menu on the configuration menu.

### 2.3.6 Digital Outputs

Choose View → Digital Outputs from the Text Menu, and then the digital output view such below <Figure 2-79> appears.

<Figure 2- 98> Example of Digital Outputs

| A shortcuts comes up (see <Figure 2-99>) when you press the right mouse button on the selected list of digital input view. To move to Digital Output Detail View, choose , Digital Output Detail menu or double click on the left side of a mouse in the selected tag. For more information, refer to chapter 2.3.6.1. | <Figure 2- 99> Shortcut Menu of Digital Output View |
| --- | --- |

| Hitting button from the Menu or ‘Change Value’ in the shortcut menu can make values set for digital output tag in the dialog box <Figure 2-100> output. | <Figure 2- 100> Dialog Box to Change Digital Output Values |
| --- | --- |

The button  from menu is to install whether to use selected tag or not.

Pressing  or ‘Tag Properties’ makes it possible to change properties for digital output tags in the dialog box as following <Figure 2-101>.

<Figure 2- 101> Dialog Box to Change the Tag Property of the Dialog Output

Users can find tags they want, when inputting tag names or sequence numbers by hitting ‘Tag Search’ from the shortcuts and install color of background, text, tag, explanation and font, its size, etc. for Digital Output View in Font and Color from Configuration Menu.

#### 2.3.6.1 Digital Output Details

Digital Output Details displaying real- time trend diagnosis and set points for digital output current values as below <Figure 2-102> can be moved from Digital Outputs, Entire Tags, Registered Groups, scripts, etc.

<Figure 2- 102> Example of Digital Output Details

| By hitting the right side button on a mouse, the shortcuts <Figure 2-103> appear. | <Figure 2- 103> Shortcut Menu for the Detailed View Screen of Digital |
| --- | --- |

The values set in output tags can be output by selecting  button or ‘Digital Output Value Change’ from the shortcut menu.

Tag properties are changeable in case of choosing ‘Tag Properties’ Change button.

Clicking Page Up or Page Down shows previous or next tag for digital input on the trend diagnosis screen. The background and text color, font and the size, etc. are set in Font or Color from Text menu in Configuration menu.

### 2.3.7 String Tags

Press ‘View | String Tags’ from the Text Menu, and then the string tags view as below <Figure 2-104> comes up.

<Figure 2- 104> Example of String Tags View

| String Tag View is the screen possible to indicate all tag names, tag explanations, current values, setting status, etc. for output tag and to change tag contents. Shortcuts such as <Figure 2-105> are displayed by clicking the right side mouse button on the selected list from the string tag view. | <Figure 2- 105> Shortcuts for String Tag View |
| --- | --- |
| Users are able to change current string values in dialog box <Figure 2-106> when double clicking one of , ‘Change Value’ from the shortcuts or the left mouse button on the selected tag. | <Figure 2- 106> Example of Dialog Box for String Change |

The Maximum string length available to input in string tag is 255 English Characters.

The button  from menu is to install whether to use selected tag or not.

Properties for string tags can be changed in the dialog box <Figure 2-107> by hitting  or ‘Tag Properties’ from the shortcuts.

<Figure 2- 107> Example of Dialog Box for String Tag Property Change

Users are able to find tags they want, when inputting tag names or sequence numbers by hitting ‘Tag Search’ from the shortcuts and install color of background, text, tag, explanation and font, its size, etc. for String Tag View in Font and Color from Configuration Menu.

### 2.3.8 View Registered Groups

Clicking ‘View | Registered Groups’ from the Text Menu displays screen such as <Figure 2-108>.

<Figure 2- 108> Example for Registered Groups View

Registered Group View is a screen to monitor and control analog, digital, string tags voluntarily registered by users.

| Clicking the right mouse button on the selected group from registered group view shows shortcuts such as <Figure 2-109>. Detailed View is available by double clicking , ’Detail’ from the shortcuts or the left mouse button on the selected list and chapter 2.3.8.1 has more information. | <Figure 2- 109> Shortcuts for Registered Group View |
| --- | --- |

Selecting ,  or ‘Insert Group’, ‘Add Group’ from the shortcuts makes it possible to insert or add new groups in the dialog box <Figure 1-110>.

<Figure 2- 110> Example of Dialog Box to Add Groups

Registered groups are changed by pressing  button or ‘Modify Group’ from the shortcuts.

| The dialog box <Figure 2-111> appears to confirm whether to delete registered groups by clicking or ‘Delete Group’ from shortcuts. | <Figure 2- 111> Dialog Box for Confirmation to Delete Groups |
| --- | --- |

#### 2.3.8.1 Detailed View of the Registered Group

Detaild View of the Registerd Group displays tag names, descriptions, current values, properties, etc. for registered tags such as <Figure 2-112>.

<Figure 2- 112> Example of Registered Group Detailed View

| Pressing the right mouse button on the selected group from registered group detailed view displays shortcuts such as <Figure 2-113>. Detailed monitor screens for each tag can be moved by clicking , Detail View, or double clicking the left mouse button, and dialog boxes to modify tag properties are open by pressing string tags. See menu buttons and shortcuts explanations for analog input and output, digital input and output, string tags to have more information about various Menu for registered group view. Color of background, tag, explanations, text and font type, size, etc. are set in Font or Color from Text Menu in the configuration menu. | <Figure 2- 113> Shortcuts for Registered Group Detailed View |
| --- | --- |

### 2.3.9 Alarm Files

Alarm Files View displaying names and the number of alarms by date such as <Figure 2-114> is shown by selecting ‘View | Alarm Files’ on Text Menu.

<Figure 2- 114> Example of Alarm Files View

| Press the right mouse side button on the selected list from Alarm View, the shortcut menu <Figure 2-115> appears. Clicking , or ‘View Alarm List’ menuitem from the shortcuts or double clicking the left mouse button on the selected list can move screens to view alarm content and chapter 2.3.9.1 has more details. | <Figure 2- 115> Shortcuts for Alarm View |
| --- | --- |
| Choosing or Delete Alarm File displays the dialog box <Figure 2-116> to confirm whether to delete alarm files. | <Figure 2- 116> Dialog Box to Confirm Whether to Delete Alarm Files |

#### 2.3.9.1 Alarm List View

‘Alarm List’ screen available to move to Alarm View or Script shows generated alarms on chosen date by categorized level, date, time, tags, explanations, alarm contents etc. such below <Figure 2-117>.

<Figure 2- 117> Example of Alarm Content View

| Use the right mouse button to bring up shortcuts <Figure 2-118> on Alarm Content View. | <Figure 2- 118> Shortcuts for Alarm Content View |
| --- | --- |
| When the Alarm Priority button or Select from the short cut menu is pressed, the dialog box <Figure 2-119> appears. Choosing an alarm priority you want in the dialog box <Figure 2-119>, the alarm content set is displayed. | <Figure 2- 119> Example of Dialog Box to Select Alarm Priorities |

button or ‘Print’ provides a dialog box <Figure 2-120> available to print out the current alarm content view screen in the set printer by clicking  after installing printer types to use, number of copies, etc.

<Figure 2- 120> Example of Dialog Box for Printing Alarm Content

Specifying months, days and years using ‘ViewAlarmList’ script functions displays alarm contents for over 2 days.

### 2.3.10 Alarm Events

Alarm View by date such as <Figure 2-121> is shown by selecting ‘View | Alarm Events’ from the Text menu.

Alarm types displayed in alarm event window are set by selecting ‘During alarm’ or ‘Until users confirm’ buttons in screen alarm types from ‘Config | Alarm Priority’ menu in Studio.

When alarms depending on priority are generated by installing ‘Config | Config Alarm’, the alarm event window can be automatically displayed on monitor screen.

<Figure 2- 121> Example for Alarm Event Window

Generally, an alarm event window possible to be input in elements on graphic monitor screen is created in toolbar window to confirm raised alarms.

| Shortcut Menus such as <Figure 2-122> are indicated by pressing the right side mouse button on the selected list from alarm event window. Alarm confirmation is available using one of ‘Confirm One Alarm’, ‘Confirm One Page’, ‘Confirm All Alarms’ from the shortcut menu <Figure 2-122> or scripts. | <Figure 2- 122> Shortcut Menus for Alarm Event Window |
| --- | --- |

Clicking one of ‘Delete Alarm’, ‘Delete All Alarms’ buttons or script makes it possible to delete raised alarms.

It is available to sound or stop alarms by selecting either ‘Disable Alarms’ or ‘Alarm Sound’ from shortcut menu in event window.

Choosing ‘Sound Alarms’ from shortcut menus in event window or setting in ‘Config | Config Alarm’ menus is to decide whether to sound alarms or not.

### 2.3.11 Log Files

Click on ‘View | Log Files’ from Text Menu to display Log View screen by date such as <Figure 2-123> showing generated log dates and file names.

<Figure 2- 123> Example of Log Files View Screen

| The right mouse button on the selected list opens shortcut menu such as <Figure 2-124>. Log Content screen can be moved by pressing or ‘View Log List’ or double clicking the left mouse button on the log list and chapter 2.3.11.1 includes more information. Clicking or ‘Delete Log File’ from buttons provides the dialog box <Figure 2-125> to confirm again whether to delete log files. | <Figure 2- 124> Shortcut Menu for Log View <Figure 2- 125> Dialog Box to Confirm Whether To Delete Log Files |
| --- | --- |

#### 2.3.11.1 Log List View

Log List View <Figure 2-126> available to move to Log View screen and scripts shows start, close information for programs and communication information, etc.

<Figure 2- 126> Example to View Log List

| Use the right mouse button to bring up shortcut menus <Figure 2-127> on Log List View. The set printer can print the current log content view screen by choosing button or ‘Print Logs’ from the shortcut menus. | <Figure 2- 127> Shortcut Menus for Log List View |
| --- | --- |

### 2.3.12 Scripts

Selecting ‘View | Scripts’ from Text Menu displays script continuously while the monitor program such as <Figure 2-128> written in Studio runs.

<Figure 2- 128> Example for Scripts View

| Shortcut Menus such as <Figure 2-129> are shown by using the right side mouse button on the selected list from script view screen. Use from script menu buttons to run or stop scripts. | <Figure 2- 129> Shortcut Menus for Scripts View |
| --- | --- |

A dialog box such below <Figure 2-130> appears, when the left mouse button is double clicked on  button, ‘Script Details’ from the shortcut menu or the selected lists.

<Figure 2- 130> Example of Dialog Box for Script Details View

The above screen of <Figure 2-130> shows script content and the below one displays the types, names, the current values for set values types.

### 2.3.13 Communication Server

Selecting ‘View | Communication Server’ from Text Menu shows communication server running files after activation and chapter 3 includes manuals to use communication programs.

### 2.3.14 Reports

This menu is to confirm and print out report results written in Studio.

| Pressing ‘View ¦ Reports’ from Text Menu opens a dialog box <Figure 2-131>. Report View <Figure 2-132> is shown by selecting report files using the dialog box <Figure 2-131>, scripts, etc. | <Figure 2- 131> Example of the Dialog Box to Open Report Files |
| --- | --- |

<Figure 2- 132> Example for Report View

Clicking  makes the current report contents print out.

Select  to display Preview about the contents to print out.

Pressing either  or  makes it possible to zoom in and out of report contents by 10 % ~ 200 %.

Use  to set standard time for Report View in <Figure 2-133>.

<Figure 2- 133> Dialog Box to Set Standard Time for Report View

Modifying the standard time for Report View is available using  and renewing report contents is possible by choosing .

The standard time for Report View is changeable into the current time using .

Reports made in Studio can be automatically printed out at regular intervals set ‘Config | Automatic Report Print’ Menu and Chapter 2.4 has more details.

### 2.3.15 Demand Controls

Demand Graph, one of elements to display graph concerning demand controls status for power control, is used to analyze power flow and an amount of power for 15 minutes.

Choosing ‘View | Demand Controls’ from the Text Menu indicates demand controls items registered such as <Figure 2-134> and demand window for selected items.

<Figure 2- 134> Example for Demand Controls Screen

Comments for Demand Window of graphic elements is also applied to the Display Principles because Demand Windows on Demand Controls and for graphic elements are identical.

Studio is responsible for setting demand items displayed on demand controls window, demand height tags for each item, tags for reading time flow, the current values, installing standards, the total time for graph, font, background color, etc.

### 2.3.16 Milli-Datas View

Milli-Datas View displays graph such as <Figure 2-135> concerning data that installed analog or digital tags are saved in MDB File at 1 ~ 60,000 mSec intervals.

<Figure 2- 135> Example for Milli-Datas View

The upper window of Milli-Datas Data View shows all data collected and the lower one displays data values for selected area in the upper one.

The area to display on the lower screen is chosen by moving a mouse with still pressing the left mouse button on the upper one.

Pressing the left mouse button on tag name display modifies the selected tag into the standard tag and clicking the right one sets whether to show graph on the lower window.

button from Menu on Milli-Data View is to import data to show in the dialog box <Figure 2-136>.

<Figure 2- 136> Example for Milli-Data View

| button enables you to set time display for Milli-Data View as well as background color in the dialog box <Figure 2-137>. Users are able to set data collection tags, intervals, conditions, Fonts, display color, etc. in Studio. Additionally, writing scripts such as MilliDataSetFile, MilliDataSetTimeType, etc. in Studio makes it possible to install display data selection and time base display methods for milli-data window. | <Figure 2- 137> Example of Dialog Box for Milli-Data View Settings |
| --- | --- |

### 2.3.17 Schedules

Schedule allows users to register running lists in advance to work at the set time each year, month, week, day to automatically control operations mainly used for Lighting Control. Choose ‘View | Schedules’ from Text Menu to display a monthly schedule <Figure 2-138> below.

<Figure 2- 138> Example of Schedule Screen

Adding or subtracting months on annual schedule screen is available from  in the <Figure 2-138> and schedule control lists for each date can be checked by pressing left mouse button on a day (1~31) for selected months.

The lower right screen for schedule displays today control lists, control contents for each list, whether to control instruments or not.

Generally, schedule is set according to the following order.

Choosing  or ‘Config | Schedule | Yearly Fixed Schedule’ displays the dialog box <Figure 2-139> to set annual fixed schedules.

<Figure 2- 139> Example of Dialog Box for Yearly Fixed Schedules

Users are able to set additional annual schedules in the dialog box <Figure 2-140> by selecting  or ‘Configuration | Schedule | Yearly Additional Schedule’.

<Figure 2- 140> Example of Dialog Box for Yearly Additional Schedule

<Figure 2- 141> Example of Dialog Box for Daily Operating Model

Pressing  or ‘Config | Schedule | Model’ menu item opens the dialog box <Figure 2-141> possible to set daily operating models.

Users are able to register the maximum number of 32767 different tags in a daily operating model to set daily running time, time stopped working, etc. at specific running points.

| or ‘Config ¦ Schedule ¦ Weekly Schedule’ button can be used to display the dialog box <Figure 2-142> available to set weekly schedules. Weekly schedules are to register fixed schedule set on each day (Sunday ~ Saturday, Holiday, Special Day). | <Figure 2- 142> Example of Dialog Box for Weekly Schedule Settings |
| --- | --- |

### 2.3.18 DB Integrations

DB Integrations shows integrated values of data saved as database data for previous and this year, previous and this month, previous and this day, previous and this time in run program.

<Figure 2- 143> Example of Dialog Box for DB Integration

Pressing ‘View | DB Integrations’ from the Text menu will open the dialog box for DB Integration Data View such as <Figure 2-143>.

DB Integration means PI Integration as well.

Data to display DB Integration can be added or deleted in the dialog box <Figure 2-144> by clicking ‘File | List Settings’ in <Figure 2-143>.

<Figure 2- 144> Example of Dialog Box for DB Integration List Settings

<Figure 2-145> appears by choosing  button from <Figure 2-144>.

<Figure 2- 145> Dialog Box to add DB Integration Lists

DB Integration Lists are added by selecting saved lists and integration tags in <Figure 2-145> for database registration in run programs.

Saved lists and integration tags are required to add DB Integration Lists.

The  button in <Figure 2-144> can be used to erase selected DB Integration Lists.

### 2.3.19 Navigation

Navigation is a screen to display entire graphic monitor such as <Figure 2-146> for the current activated MDI property.

<Figure 2- 146> Example of Navigation Screen

Holding the left mouse button and moving it left or right will show rectangles available to enlarge or reduce the current screen depending on the image size of the selected rectangle.

## 2.4 Descriptions by Each Menu

The Menu bar consists of File, View, Config and Help on monitor programs.

The menu order can be changed by either choosing scripts or modifying ‘menu.mnux’. (Refer to the edit program manual.)

### 2.4.1 File Menu

| File Manu has Login, Logout, Write Memo, Read Memo, Print Screen, Save Screen, Save Selection Zone, Run Studio such as <Figure 2-147>. | <Figure 2- 147> File Menu |
| --- | --- |

#### 2.4.1.1 Log In

Log In is to leave use records and for system security when several users use in a system.

Choosing login from File Manu opens user login dialog box <Figure 2-148> available to input the username and password made by the manager for login.

Managers are able to give users their usernames, password, permission, etc. and the manager username and the initial password are ADMIN.

<Figure 2- 148> Example of Log In Dialog Box

The username and password should be less than 39 characters with English letters and numbers.

Managers are able to register, change users, give authorization and modify passwords for each user from ‘Config | Config Users’ menu.

#### 2.4.1.2 Log Out

This is to set only ‘monitor program view’ without logged in users.

The username logged out is _PUBLIC_ using Logout from File Menu.

#### 2.4.1.3 Write Memo

The dialog box such as <Figure 2-149> appears by clicking ‘Write Memo’ menu to write emails to other users.

<Figure 2- 149> Example for Writing Memo

After writing memo titles and contents, press ‘Send’ with choosing users to receive it.  If you want to send emails several users at a time, select usernames in ‘Send To’.

#### 2.4.1.4 Read Memo

<Figure 2-150> opens up by selecting the ‘Read Memo’ menu available to read emails received from other users or getting email from logged in users when you log in.

<Figure 2- 150> Dialog Box to Read Memo

After selecting an email list in <Figure 2-150>, press  or double click the left mouse button to read emails.

Use button to erase the selected memo.

#### 2.4.1.5 Print Screen

Print Screen are to print the current window screens as bitmap graphics formats, and the dialog box <Figure 2-151> comes up by pressing ‘Print Screen’.

<Figure 2- 151> Dialog Box to Print Screen

Screen Printing is completed successfully by clicking  buttons, after adjusting the image area on the left side of <Figure 2-151> to print out and setting types of printers.

You can set paper size, orientation, margins, the printer, etc. using  in ‘Print Screen’ dialog box.

It is available to print images in reverse order by clicking on  and also save and load setting contents to print screens with  and  buttons.

#### 2.4.1.6 Save Screen

The current windows screen can be printed with bitmap graphics formats using BMP and JMP available to be saved.

#### 2.4.1.7 Save Selected Screen

This feature is to save the only selected region on the current windows screen as bitmap graphics formats.

To open the dialog box such below <Figure 2-152>, press Save Selected Screen form File Menu.

<Figure 2- 152> Dialog Box to Save Selected Screen

If you click to check  or  in <Figure 2-152>, you can modify images in reverse order or choose the entire screen. It is available to save and load setting contents for saving on the selected screen by pressing  or  button.

Selected images can be saved as Bitmap (BMP, JPG) using button after choosing image areas to save in <Figure 2-152>.

#### 2.4.1.8 Run Studio

Only authorized users are able to run Studio after closing down the monitor program.

Choosing ‘Run Studio’ on graphics monitor screen is to run Studio available to modify current graphics screens, and on tag monitor screen possible to move to Studio keeping edited tags. And Studio is run with edited scripts in script monitor.

#### 2.4.1.9 Exit

The dialog box <Figure 2-153> is to ask whether you close the monitor program or not.

Outsiders who do not have permission ‘Close’, or unauthorized are not able to close monitor program.

<Figure 2- 153> Dialog Box to Ask Whether to close Monitor Program

### 2.4.2 View

View Menu contains commands such as Graphics, Entire Tags, Analog Input, Analog Output, Digital Input, Digital Output, String Tags, Registered Groups, Alarm Files, Alarm Events, Log Files, Scripts, Communication Server, Reports, Demand Controls, Milli-Datas, Schedules, DB Integrations, Navigation.  For more information, refer to chapter 2.3.

### 2.4.3 Config

| Necessary data, Font size, screen status, etc. to run monitor program are set in Config text menu including sub menus such as Config Alarm, Config Font, Config Colors, Config Data, Config Flow Watch, Config Users, Config Other, Config Excel Path, Database, Schedule, Automatic Report Print. | <Figure 2- 154> Config Menu |
| --- | --- |

#### 2.4.3.1 Config Alarm

The following dialog box <Figure 2-155> appears when you click ‘Config | Config Alarm’ Text Menu.

<Figure 2- 155> Dialog Box to Set Configuration for All Alarm

Users are able to set whether to Disable all alarms, alarm sound, alarm smessage, Alarm Filters, Alarm when manual operation failed, Digital tag output when alarms occur, etc.

#### 2.4.3.2 Config Font

Clicking Config Font from Config Text Menu opens up the dialog box <Figure 2-156> to set Fonts available to change fonts and font size on Windows screens.

<Figure 2- 156> Dialog Box to Select Font

#### 2.4.3.3 Config Colors

Config Colors buttons on Config Menu bring up a submenu to set all colors and alarm colors.

| 1) Basic Colors Pressing Basic Colors button is available to open up the Dialog Box <Figure 2-157> to set Text, Background, Tag, Description, Inactive, HiHi, High, Low, LoLo, ON, OFF Color, etc. | <Figure 2- 157> Dialog Box to Set Basic Colors |
| --- | --- |
| 2) Alarm Colors By clicking Alarm Colors, <Figure 2-158> comes up to set colors for HiHi, High, Low, LoLo, DI ON, DI OFF, Return, Manual Operation, Demand Control, etc. | <Figure 2- 158> Dialog Box to Set Color |

#### 2.4.3.4 Config Data

To bring up the dialog box <Figure 2-159> below, choose Config Data button from Config Text Menu.

<Figure 2- 159>> Dialog Box to Set Data Management

Users can set whether to save all data, Data directory, days to keep data, intervals to save minute data, start saving data, duplex server data, etc. in dialog box <Figure 2-159>.

Assigned directories are to save data for time, minutes, log, alarms, etc. and start time for storing data aims to save data after setting time to get correct data with running monitor program. If Intervals to Save Minute Data are set with 10 minutes, users are able to save time for storing data.

#### 2.4.3.5 Config Users

Choosing Config Users from Config Text Menu brings up <Figure 2-160> below available to register new usernames, delete users and set user permissions and password, etc.

<Figure 2- 160> Dialog Box for User Settings

The following <Figure 2-161> to set usernames, web settings, control tag registration, etc. comes up by selecting  or  button in the dialog box for user settings.

<Figure 2- 161> Dialog Box for Setting User Properties

Deleting registered users and changing user passwords are available by clicking  or  button.

Permission to delete users is given to only the manager and password changing is available by the manager and the user oneself.

To set the default logon user and the manager password, select administrator item tab in the dialog box for user settings.

#### 2.4.3.6 Config Other

When you choose Config Other Settings from Config Menu, the following dialog box <Figure 2-162> appears. And it is to set ‘Display tool tip on tag object’, ‘Align to window edge’, ‘Respond to left mouse click on graphics module’, ‘Respond to right mouse click on graphics module’, ‘Use menu buttons on graphics module’, ‘Max MDI Window Control’, ‘Match to display format in AI calculation’, ‘Pause Scan’, ‘Scan Start Time’, ‘Close Communication Server when closing this program’, ‘Display Prompt box when closing this program’, etc.

‘Scan Start Time’ indicating starting time to regularly operate monitor and communication programs, is generally set for 5~30 seconds input for each second.

<Figure 2- 162> Dialog Box for Other Config

#### 2.4.3.7 Config Excel Path

Clicking ‘Config Excel Path’ necessary for script functions related to Excel Report from Config Text Menu brings up <Figure 2-163> available to set the route including Excel Program Executable File, Microsoft.

<Figure 2- 163> Dialog Box for Excel Path Settings

#### 2.4.3.8 Database

Sub Menu for connection string and shared database appears by selecting Database button from Config Menu.

1) Connection String

Connection String is to set database types and names to connect with database in functions related to database for script and run programs.

<Figure 2-164> is available to set connection strings depending on database types.

<Figure 2- 164> Dialog Box for Connection String Settings

or  button in <Figure 2-164> brings up <Figure 2-165> possible to add or modify connection strings by inputting the titles, database types and connection strings for each database.

Refer to database program manuals and Help to set connection strings input different according to database types such as an example of <Figure 2-165>.

<Figure 2- 165> Example of Dialog Box to Add or Modify Connection Strings

2) Shared Database

This feature is to share current values and tags for monitor programs with external systems by storing tag names and current values in table ‘TAG’ and ‘CURR’ column.

Users are able to set connect strings depending on database types in <Figure 2-166> by pressing shared database.

When you check Able in dialog box <Figure 2-166>, raised alarms are to be read from external programs by saving them in the database table.

<Figure 2- 166> Dialog Box for Shared Database Settings

#### 2.4.3.9 Schedules

Clicking Schedules menu from Config Text Menu displays sub menu such as settings for Yearly Fixed Schedules, Additional Annual Schedules, Models, Weekly Schedules.

Each menu for schedule control is equal to menu button setting for ‘View | Schedules’ and therefore you can refer to annual schedule comments to use.

#### 2.4.3.10 Automatic Report Print

This feature is to print automatically set reports hourly, daily, monthly and the following <Figure 2-167> shows the settings item to print report automatically currently set.

<Figure 2- 167> Dialog Box to Automatic Report Print

Selecting or  button in <Figure 2-167> opens up the dialog box <Figure 2-168> to add or modify the feature to print report automatically.

<Figure 2- 168> Dialog Box Example to Add or Modify Function to Automatic Print Report

Adding or modifying function to print report automatically is available by inputting report file names, printer names and automatic print cycle in <Figure 2-168>.

Two types of report files are available to be set for automatic report print.  One is the default report written in Studio and the other is written with the excel report function.

### 2.4.4 Windows

| When you click on Window menu from monitor program, the menu pulls down, revealing a list of menu item <Figure 2-169> such as Cascade, Tile Horizontally, Tile Vertically, Arrange Icons, Close, Close All. Refer to Window Manuals because the instructions between each sub menu from Window Menu and original Window menus are same. | <Figure 2- 169> Windows Menu |
| --- | --- |

### 2.4.5 Help

| Pressing Help Menu brings up the dialog box <Figure 2-170> showing Help, Remote AS, UserName?, Keylock Information, About?. | <Figure 2- 170> Help Menu |
| --- | --- |

#### 2.4.5.1 Help

‘Help’ can be chosen in each dialog box by clicking on ‘Help’ button.

| 2.4.5.2 UserName? The dialog box <Figure 2-171> by choosing Username? Displays currently logged in username. | <Figure 2- 171> Example of the Dialog Box to View Username |
| --- | --- |

#### 2.4.5.3 Keylock Information

The dialog box <Figure 2-172> displays the keylock Information by selecting Keylock Information Menu.

<Figure 2- 172> Dialog Box for Keylock Information

#### 2.4.5.4 About?

By selecting ‘About’ Menu, <Figure 2-173> comes up revealing program names, versions, development company, etc.

<Figure 2- 173> Dialog Box for Program Information

<Empty Page>

# Chapter 3. Communication Server

Communication Server specify how to communicate with Controller or PLC and memory address and size read from them.

Communication Servers move the data acquired by communicating with PLC or Controllers in the diagram <Figure 3-1> below into memories for them and send it to monitor programs when requested.

<Figure 3- 1> Communication Server Diagram

## 3.1 Communication Server Running

Select ‘Communication Server’ () from AutoBase Windows or Start Program to run communication server.

Communication Server is run automatically when monitor programs are operated with communication mode.

## 3.2 Whole Figure and Shortcuts Descriptions

### 3.2.1 Whole Figure Descriptions

When you run communication server, the screen <Figure 3-2> appears.

<Figure 3- 2> Initial Screen for Communication Server

#### 3.2.1.1 Title Bar

This is an original window feature to display names such as <Figure 3-3> on upper screen.

<Figure 3- 3> Title Bar

#### 3.2.1.2 Menu Bar

The Menu Bar includes File, View, Config, Window and Help from Communication Server.

Users are able to select menus they want by moving the mouse and clicking the left mouse button on Text menu items, or pressing ‘Enter’ on menu items with pressing ‘ALT’ or ‘F10’ on keyboard.

#### 3.2.1.3 Menu Button

Menu buttons are displayed below the horizontal scroll bar from Communication Server.

#### 3.2.1.4 Windows Internal Area

Windows Internal Area displaying contents for communication server is changed depending on screen types.

### 3.2.2 Shortcuts Descriptions

Keyboard Shortcut Summary in communication server is shown below in <Table 3-1>.

| SHORTCUTS | FUNCTIONS |
| --- | --- |
| ENTER | Select functions and check menus, etc. |
| ESC | Cancel functions and move back to previous the menu. |
| ,,, (arrow keys) | Move between menus. |
| ALT, F10 | Move to the Menu Bar. |
| SHIFT+F5 | Cascade MDI Windows |
| CTRL+F4 | Close the MDI Window currently selected. |
| PGUP, PGDN, Other FUNCTION Keys | Use differently for each monitor screen. |
| Other Default Shortcut Keys | Default Shortcut Keys for Windows |

<Table 3- 1> Shortcut Descriptions for Communication Server

## 3.3 Descriptions for each Menu

The Text Menu consists of File, View, Config, Window, Help on communication server.

### 3.3.1 File Menu

| File Menu includes sub items such as ‘Edit Port File’, ‘Bit Write’, ‘Word Write’, ‘Virtually Write’, ‘Close’ in <Figure 3-4>. | <Figure 3- 4> File Menu Item for Communication Server |
| --- | --- |

#### 3.3.1.1 Modify Communication Ports

The dialog box <Figure 3-5> to choose communication ports comes up by selecting ‘Edit Port File’ button from File Menu.

<Figure 3- 5> Dialog Box to Choose Communication Port.

Clicking on communication ports in <Figure 3-5> to set opens up <Figure 3-6> to edit communication files.

Users are able to refer to chapter 3.4 and 3.5 to edit it.

<Figure 3- 6> Dialog Box to Edit Communication File

#### 3.3.1.2 Bit Write

‘Bit Write’ buttons function to test Bit Control for controller and PLC linked to the specified communication port without connecting to the monitor program.

| Clicking on ‘Bit Write’ brings up <Figure 3-7> to test it by setting communication ports to output, stations, address, extra 1, extra 2, etc. | <Figure 3- 7> Dialog Box to Write Bit |
| --- | --- |

#### 3.3.1.3 Word Write

‘Word Write’ button is to test word, double word and float values for controllers or PLC connected to specified communication ports without linking to the monitor program.

| Users are able to set communication ports to output, stations, address, extra 1, extra 2, etc. to test write word in <Figure 3-8>. | <Figure 3- 8> Dialog Box to write word |
| --- | --- |

#### 3.3.1.4 Virtual Write

‘Virtual Write’ button has a function to change only communication memory values for WORK, FLOAT, DWORD without outputting on PLC or Controller.

<Figure 3-9> comes up by selecting ‘Virtual Write’ button to set ports, address, memory types and writing values for communication memory for Virtual Write.

<Figure 3- 9> Dialog Box for Virtual Writing

#### 3.3.1.5 Exit

Press ‘Exit’ button to close the communication server.

You should not close the communication server available to communicate with PLC to monitor regularly.

### 3.3.2 View Menu Items

View Menu Items consist of sub menus to display Main Program, Memory, Communication Code (Hex), Communication Code (ASCII), Port Status, Network Memory Server, DLL Protocol Information.

#### 3.3.2.1 Main Program

Selecting ‘Main Program’ button activates or runs the monitor program.

#### 3.3.2.2 Memory

Real communication memory read from PLC or Controllers can be displayed by choosing ‘Memory’ such as <Figure 3-10> according to the order of WORD/FLOAT/DWORD /STRING/SYSTEM.

<Figure 3- 10> View Memory Structure

Pressing  button shows communication memory types depending on the changed order of WORD, FLOAT, DWORD, STRING, SYSTEM and clicking on  or  displays them with modified communication ports.

Comm Try, Code Bad and Time Out for current communication ports are displayed on the bottom of the screen to show communication status for each communication ports.

The data such numbers of communications, etc. is for a day and communication results are saved in log.

#### 3.3.2.3 Communication Code into Hex

Code in current communications is changed into HEX using ‘Communication Code (Hex)’ button on screen in <Figure 3-11>.

Communication Code View is displayed in Hex or ASCII format by choosing  from View Menu.

After pausing View, pressing again  makes it possible to view communication code, however communication continues during the pause.

<Figure 3- 11> Example to View Communication Code in Hex

Users are able to choose communication code view for different ports by clicking on the area displayed with numbers such as 000, 001 on the left side of screen and currently set communication port number in <Figure 3-11>.

#### 3.3.2.4 Communication Code into ASCII

This button including a similar feature with Communication Code (ASCII) shows communication code into ASCII format.

#### 3.3.2.5 Port Status

When you click on ‘Port Status’ from View Menu, <Figure 3-12> comes up to display names, telephone number, Device settings, total counts of communications ,bad code and timeouts, etc. for ports from No. 0 to No. 255.

,  and  buttons are only available using dial-up connection for set communication ports.

<Figure 3- 12> Screen to View Port Status

#### 3.3.2.6 Network Memory Server

<Figure 3-13> displaying setting status screen for network server appears by pressing ‘Network Memory Server’ button.

<Figure 3- 13> Screen for Network Memory Server Status

Network memory server directly sends communication memory contents to other computers via ports for connection number 0 to 255.

Double clicking the left mouse button on the connection numbers in <Figure 3-13> brings up the dialog box <Figure 3-14> to set Connection Type, Serial Port Settings, Items counts for one time,  Send Delay, etc. for network memory serer.

<Figure 3- 14> Dialog Box to set connection for network memory server

The chapter 4 will help you understand concepts of communication and types of settings for network memory server and client.

#### 3.3.2.7 DLL Protocol Information

Clicking on DLL Protocol Information button from View Menu items shows the filename, protocol, date, file size, version, etc. for communication protocol currently registered as following as in the following <Figure 3-15>.

Press  to upgrade all DLL Protocol in Protocol folder which is a subfolder for running file folder.

Copy developed DLL file in the Protocol folder in case a new protocol file might be developed and choose  button to register one.

<Figure 3- 15> Dialog Box for DLL Protocol Information

### 3.3.3 Config Menu Item

| Config Menu Items consists of submenus such as Options, Editor Font and Modem Options as follows <Figure 3-16>. | <Figure 3- 16> Configuration Menu |
| --- | --- |

#### 3.3.3.1 Options

If you click on ‘Options’ button, the <Figure 3-17> appears available to set Message Screen, Communication Delay Time, etc.

‘MultiPort MultiTasking’ in <Figure 3-17> is to set whether to try Port Read for another port after reading one in several ports.

Using MultiTasking in several serial communications makes all communication speed faster.

Additionally, scan count in Manual/SetVipScan is set to manually output or read VipScan Points specified with scripts of the monitor program faster than other points.

<Figure 3- 17> Dialog Box to Set Total Configuration

#### 3.3.3.2 Editor Font

Fonts available in protocol settings can be set using Editor Font button from Config Menu Items.

#### 3.3.3.3 Modem Options

You are able to set initial commands for modem ports to dial up connection by choosing ‘Modem Options’ Menu.

### 3.3.4 Windows Menu Items

Window Menu Items similar to the original functions for MDI Windows includes submenus to Cascade, Tile Horizontally, Tile Vertically, Arrange Icons, Close All and select open windows as follows. (See <Figure 3-38>)

<Figure 3- 18> Windows Menu Items

### 3.3.5 Help Menu Items

The Help Menu Items contain submenus such as Help, Using Help and System Information in <Figure 3-39>.

<Figure 3- 19> Help Menu Items

#### 3.3.5.1 Help

If you click on either Help, F1 buttons from Help Menu Items or the Help button in dialog boxes, Help for the communication server appears.

#### 3.3.5.2 Using Help

Users are able to see the basic help usage provided in Windows by selecting the ‘Using Help’ button.

#### 3.3.5.3 System Information

By pressing the System Information button, the <Figure 3-20> comes up displaying writing values and numbers of writing items waiting in the dialog box below.

The writing items waiting are waiting in the communication server not output in points controlled with manual control, scripts, etc. from the monitor program.

<Figure 3- 20> Dialog Box for System Information

## 3.4 Communication Setting Method

The Communication Setting Method is to set communication devices, protocol, types of reading, etc. between field equipment and communication server.

### 3.4.1 Device

Generally used communication device contains Serial(RS-232C, RS-485, RS-422), Network (TCP/IP, UDP/IP), input/output card with built-in computer, Field Bus, Profi Bus, OPC or other communication formats.

#### 3.4.1.1 Serial

Serial devices used in usual COM port communication include RS-232C, RS-485, RS-422, etc.

RS-485 or RS-422 communication is recommended in long distance communication (over 15 m) instead of the type of RS-232C not dependable for accuracy.

Using Exclusive cards for communication or RS-232 ~ RS-485/RS-422 communication converters is required for RS-485 and RS-422 communication.

The following <Figure 3-21> ~ <Figure 3-23> are 9 pin and 25 pin standard communication cable connection diagram for RS-232C communication.

<Figure 3- 21> RS-232C 9pin~25pin communication cable connection diagram

<Figure 3- 22> RS-232C 9pin~9pin communication cable connection diagram

For more information about cable connection methods, refer to manuals for equipment in case that serial communication cables such as RS-232C would need different types of connection depending on kinds of machines.

The communication server and Baud Rate, Parity Bit, Data Bit, Stop Bit, etc. in serial communications must match for regular communications.

<Figure 3- 23> RS-232C 25pin~25pin communication cable connection diagram

#### 3.4.1.2 Network

LAN or network card in computers should be set for network devices.

Generally, the communication protocol for network devices uses TCP/IP and UDP/IP.

Refer to the network machine manual about LAN for network devices or communication cable wiring.

TCP/IP and UDP/IP protocols are required to set IP addresses and service ports for machines to communicate.

#### 3.4.1.3 Internal Computer Card

Internal cards are input and out cards for digital or analog (A/D or D/A card) set in computer slot.

Set machines for the internal card with referring to setting programs or manuals provided by each manufacturer.

#### 3.4.1.4 FieldBus, ProfiBus

Communications by fieldbus, profibuf or other exclusive cards use mostly private cards provided by manufacturer with setting in computers and sometimes communication converters.

Set communication connection such as fieldbus, profibus, etc. with referring to manuals provided by manufacturers.

#### 3.4.1.5 OPC

OPC Communications stand for mutual communications between programs on Windows operating systems which Send data to the monitor or communication server by communicating with OPC server program and main OPC client program (OpcClient.exe).

Refer to each OPC server program instruction for OPC server usage and use main OPC client programs with related Help.

### 3.4.2 Communication Settings

Communication server, developed on 000~255 ports randomly specified are designed to communicate with PLC and controllers.  You are able to set it with text or in communication servers displayed below.  The following dialog box <Figure 3-24> comes up by clicking on ‘Edit Port File’ button from File menu items in the communication server.

<Figure 3- 24> Dialog Box to Select Communication Port

<Figure 3- 25> Dialog Box to Edit Communication Files

<Figure 3-25> appears to set whether to use ports, threads and types of protocols and reading, etc. by clicking on the communication port to modify in <Figure 3-24>.

Each factor in <Figure 3-25> to modify communication files is the following in <Table 3-2>.

| Editing Factor | Setting Method |
| --- | --- |
| Port No. | Port numbers between 0~255 specified in port selection |
| Port Enable | Whether to currently use the port |
| Use Thread | Whether to use threads |
| Descriptions | Comments for ports, Not necessary to input. |
| Read Cycle | Input mSec as a unit for time intervals to read each read item. |
| Write Cycle | Input Msec as a unit for time intervals to output accumulated commands in write command buffers. |
| DEVICE | Input communication port numbers, TCP/IP address, speed, etc. (Refer to the chapter 4.2.1) |
| Protocol | Select created communication protocols. (Refer to chapter 3.4.2.2) |
| Option | Input additionally needed contents for each protocol |
| WORD, FLOAT, DWORD, STRING Memory Size | Input the size of the communication memory using numbers. |
| Read TimeOut | Maximum waiting time from sending a read command to get all data. |
| Write TimeOut | Maximum waiting time from a write command. to a signal displaying the command is completely written |
| Modem Option... | Settings to read remote data via modem (Refer to 3.4.2.3) |
| Line Dual | Settings to communicate with spare lines in case of errors on standard ones. (Refer to chapter 3.4.2.4) |
| Computer Dual | Settings to monitor and control 2 computers with a line (Refer to chapter 3.4.2.5) |
| Settings for Read Type | Method settings to read specific machine areas via communication memory (Refer to chapter 3.4.2.6) |

<Table 3- 2> Setting Method for each factor in Dialog Box to edit communication file

#### 3.4.2.1 Device Settings

Users are able to set devices depending on protocol types as in the following <Figure 3-3>.

| Device Types | Descriptions |
| --- | --- |
| None | Mainly Available in communication by computer internal card, field bus, floppy bus, etc. |
| Com Port | Used the most for RS-232/422/485 communication |
| Modem | Available to communicate with common modem(Com Port used for leased line modem) |
| TCP/IP, UDP/IP | Available for network communication via LAN, etc. |
| TeleDevice | Available to use machines with Modem-Device |
| NetClient | Available when communication servers running as network client are used for network repeaters |
| Shared Memory | Run programs created by communication servers and users via specified shared memory. |

<Table 3- 3> Comment to Set Device for Each Type

<Figure 3-26> to set port devices appears by clicking on the  button in <Figure 3-25>.

<Figure 3- 26> Dialog Box to Set Port Device

You can mainly use Tx, Rx flow control, RTS/DTR End Delay and Start Delay in <Figure 3-26> in 485 communications and input initialization and connection commands and connect signal timeout using button in TeleDevice.

TeleDevice is for communication equipment (radio, etc.) to command initiations and connections in communication connections and in case of communications between OPC Client Main and Communication Server uses the shared memory required to input the set name in the main program.

#### 3.4.2.2 Protocol Settings

| Protocol settings to use are available in <Figure 3-27> using button on protocol input editor screen in <Figure 3-25> to edit communication files. If you want to use protocols unlisted in <Figure 3-27>, create DLL Files with tool kit or add them by contact ing the development company. | <Figure 3- 27> Example of Protocol list |
| --- | --- |

#### 3.4.2.3 Dialup Settings

Users are able to set phone numbers to connect, connection cycles, time, whether to connect automatically, etc. in <Figure 3-28> by clicking on  button in the dialog box to edit port files.

<Figure 3- 28> Dialog Box for Dialup Settings

Dialup Connection Settings are available when communication devices use MODEM1 ~ MODEM256.

Communication servers keep calling phone numbers to connect every 60 minute (an hour), communicating with it for 60 seconds (1minute) and hanging up depending on connection cycles such as 60 minutes, 60 seconds or automatic connection.

#### 3.4.2.4 Line Duplex

Line Duplex is to communicate with reserve devices and protocols in case of the standard devices (lines) specified with a condition of automatic transfer.

Check out ‘Duplex able’ on Duplex Line Settings Area in the dialog box to edit communication files and click on  button, <Figure 3-29> to set ears.

Set Condition of line change, Secondary Device and Protocol to use, etc. in <Figure 3-29> for duplex available.

<Figure 3- 29> Dialog Box to set Line Duplex

#### 3.4.2.5 Computer Duplex

The <Figure 3-30> comes up by pressing  button with checking ‘Use Duplex’ from Computer Duplex Settings Area in the Dialog Box to edit port files.

Computer Computer is available in case of setting whether to use threads, anotuer computer information, Timeouts to change, etc. in <Figure 3-30>.

<Figure 3- 30> Dialog Box to set Computer Duplex

Duplex Computer Systems which 2 computers use for monitor and control on a line is are designed to communicate with other s systems in case the current connected computers are in transfer conditions.

In that case, systems not directly communicated share communication data via IP address or service ports specified from Computer Duplex Settings.

#### 3.4.2.6 Set Read Method

Methods to read the specific area for equipment via communication memories are either to input it (not available depending on protocol types) using the  button, or to directly input it on editor areas below.

The setting follows in the order of READ (FLOAT, DWORD, STRING), equipment station numbers, memory types for each area, the start address to read, memory storage locations for communication servers, sizes to read as below.

| Input Example) | READ, 255, DI, 2, 2, 2, |
| --- | --- |
|  | FLOAT, 255, AI, 14, 58, 4, |
|  | DWORD, 255, AI, 0, 0, 4, |
|  | ... |

PLC or Controller address to read possible to be listed can be different according to communication protocol types as above.

‘Read Command’ is used to save read data in WORD Memory and each command such as FLOAT, DWORD and STRING Command’ store them in its memory for example FLOAT, DWORK and STRING Memory.

## 3.5 Communication Status Signal

The communication server running with connecting to the monitor program displays the current communication status on the monitor program using the communication status signal.

The communication status stored in System Memory of the communication server can be checked with analog or digital tags.  Set ports and addresses as follows <Table 3-4> to display the current communication status into digital input tag, etc.

| PORT | 500 | Port Number + 1 (If Port number is 1,then 501) |
| --- | --- | --- |
| ADDRESS | 0000 | ON – normal communication, OFF – abnormal communication |

<Table 3- 4> Setting Factor for Input Tag to Check Communication State

<Table 3-5> shows the addresses and contents of status signals for main communication state saved in SYSTEM Memory.

| Port | Addr. | Motion | Remark |
| --- | --- | --- | --- |
| 500 + Port No. | 0000 | ON- Normal, OFF-Abnormal | Immediate reactions in case of communication timeout |
|  | 0001 | ON- Normal, OFF- Abnormal | Responds to 5 timeouts occurring continuously |
|  | 0002 | ON- Normal, OFF- Abnormal | Responds to 10 timeouts occurring continuously |
|  | 0003 | ON- Normal, OFF- Abnormal | Responds to 20 timeouts occurring continuously |
|  | 0004 | ON- Normal, OFF- Abnormal | Responds to 30 timeouts occurring continuously |
|  | 0010 | ON- during dial-up connection | Displays whether to dial up connection |
|  | 0020 | ON- Reserve Device, OFF- Basic Device | Device status currently being used in using duplex options |
|  | 0030 | ON- Timeout, OFF-Normal | ON in case of communication time out |
|  | 0031 | ON-Bad Code, OFF-Normal | ON in case of bad communication code |
|  | 0040 | ON- Relative Server Recognition, OFF-Relative server check not available | When recognizing the relative server in using duplex PC. |
|  | 0041 | ON- This is the Master Computer | This is the Master in using duplex PC. |
|  | 0042 | ON- The relative computer is the Master | The relative computer is the Master in using duplex PC. |
|  | 0043 | ON- Timeout occurring on this computer | Whether timeout occurs or not in this computer with duplex PC. |
|  | 0044 | ON- Timeout occurring on the relative computer | Whether timeout occurs or not in the relative computer with duplex PC. |

<Table 3- 5> Address and Contents of Status Signals

for Main Communication State Signal Stored in System Memory

<Table 3-6> shows the addresses and contents of success or failure rate for communication.

| Port | Addr. | Contents | Remarks |
| --- | --- | --- | --- |
| 500 + Port No. | 0005 | Communication Success Rate | Success Rate x 100 , Thus 0 ~ 10000 (100 %) Values |
|  | 0006 | Communication Failure Rate | Failure Rate x 100 , Thus 0 ~ 10000 (100 %) Values |
|  | 0007 | Success Rate for Basic Device Communication | Success Rate x 100 , Thus 0 ~ 10000 (100 %) Values |
|  | 0008 | Success Rate for Reserve Device Communication | Failure Rate x 100 , Thus 0 ~ 10000 (100 %) Values |

<Table 3- 6> Address and Contents of Success or Failure Rate for Communication

The following <Table 3-7> is output addresses and Contents for modem connection or reserve/basic device conversion.

| Port | Addr. | Extra1 | Description | Remarks |
| --- | --- | --- | --- | --- |
| 500 + Port No. | 0010 | #DO# | Modem Connection /Closing with ON/OFF button | Device=Modem |
|  | 0020 |  | Reserve/Basic Device Connection with ON/OFF button |  |

<Table 3- 7> Output Address and Contents for Modem Connection or Reserve/Basic Device Conversion.

<Empty Page>

# Chapter4. Network Program

AUTOBASE Network Program available to monitor or run contents supervised with AUTOBASE includes network memory server/client, network server/client, etc.

## 4.1 Network Memory Server / Client

Network Memory Server/Client as a method of sharing communication servers configures network systems.

The configuration is as in the following <Figure 4-1> and the maximum 256 clients can connect to the network memory server.

<Figure 4- 1> Network Memory Server / Client Diagram

### 4.1.1 Network Memory Server Settings

Network Memory Server Settings is to read the communication memory read from communication servers from another one.

You are able to set network memory servers in <Figure 4-2> by clicking on ‘View | Network Memory Server’ from the communication server.

<Figure 4- 2> Example of Network Memory Server State Screen

The following dialog box <Figure 4-3> to set network memory servers appears by double clicking on the left mouse button after selecting numbers you want between connection 0~255 in <Figure 4-2>.

<Figure 4- 3> Dialog Box Network Memory Server Connection Settings

Select one of NULL Modem, TCP/IP, UDP/IP for the connection methods of network memory servers.

Additionally, depending on connection methods, input serial port settings, TCP/IP, UDP/IP service port numbers and set Send Delay and Item counts for one time.

### 4.1.2 Network Memory Client Settings

Network Memory Client can be set with ‘Edit Communication File’ from Communication Servers.

Choose ‘File | Edit Port File’ menu from Communication Server and edit communication files as the following <Figure 4-4> to set Network Memory Client.

<Figure 4- 4> Example to Edit Communication File of Network Memory Client

Input connection methods (one of NULL modem, TCP/IP and UDP/IP) set in server, communication speed, IP addresses, service ports, etc. for Device and read lines in read areas and set ‘DLL-Network Client’ for Protocol in <Figure 4-4>.

Input communication port numbers (0~255) to read from server computers in protocol options and ones as much as set in servers in WORD, FLOAT, DWORD memory.

If you set the Network Memory Client such as <Figure 4-4>, you can monitor the communication memory of servers read from clients, send control commands from them to servers and do monitoring , control, alarms settings, report output, etc. by setting different tags in client systems.

## 4.2 Network Server / Client Configuration

Network Server/Client are able to create network systems in single or double environments, and the maximum number of clients available to connect to one network server is 256.

The following <Figure 4-5> displays the Network Server and Client Program Diagram.

<Figure 4- 5> Network Server / Client Program Diagram

## 4.3 Network Server

The Network Server can be set on one of a single server used in case of one server, dual primary server and dual secondary server.

### 4.3.1 Running Network Server

The Network Server Program as in the following <Figure 4-6> starts to run using AUTOBASE Windows or ‘Network Server’ () button from Start Program.

Also, you can register the Network Server along with monitor programs in the Start Program or use scripts in the monitor program to run it.

<Figure 4- 6> Example of Network Server Program Running

The Network Server consists of the program name display, text menus, Windows internal area, etc. and use general shortcuts.

### 4.3.2 Function Description for Each Text Menu

The Text Menu on the network server includes File, View, Config, Window and Help.

#### 4.3.2.1 File Menu Item

The File Menu Items contain text items to activate this computer, another computer, exit, etc. as in the following <Figure 4-7>.

<Figure 4- 7> File Menu Items of Network Server

Activate this computer or another computer button is for dual network, or activates the specified server in regular communication status.

Clicking on Exit button closes the Network Server Program.

#### 4.3.2.2 View Menu Items

View Menu Items contains sub menus such as Server State, System Memory, Client State, View Communication Code and Network Connection as below <Figure 4-8>.

<Figure 4- 8> View Menu Items of Network Server

1) Server State

The <Figure 4-6> displays connection state for set network server, connection names, monitor status, etc. by selecting Server State button from View Menu.

2) System Memory

Clicking on ‘System Memory’ button opens <Figure 4-9> showing duplex connection status, activation for each server, connection status for the network connection node 0~F(16th node) address, etc. The following <Table 4-1> is addresses and contents for system memory status of the network server.

<Figure 4- 9> Example of System Memory for Network Server

| Address | Contents | Remarks |
| --- | --- | --- |
| 0000 | Connection State of Primary and Secondary server in duplex system | 1 = Connected 0 = Disconnected |
| 0001 | This server is active in duplex system | 1 = Active 0 = Inactive |
| 0002 | The relative server is active in duplex system. |  |
| 0160 ~ 016F | The basic line state for network connection Node 0 ~ The basic line state for network connection Node F | 1 = Connection 0 = Bad |
| 0170 ~ 017F | The reserve line state for network connection Node 0 ~ The reserve line state for network connection Node F |  |

<Table 4- 1> Addresses and Contents for System Memory Status of the Network Server

3) Client State

By pressing ‘Client State’ from View Menu, <Figure 4-10> appears displaying the connected client IP address, connection status, the number of receiving/transmitting frames, etc.

<Figure 4- 10> Example of Client State View

4) Communication Code

As shown in <Figure 4-11>, these two view windows, one is the transmitting code using servers and the other is receiving code from each client or other servers can be displayed by clicking on Communication Code button from View Menu.

<Figure 4- 11> Example to View Communication Code

5) Network Connection

If you click on Network Connection button from View Menu, <Figure 4-12> appears to show the basic IP and reserve IP for each server/client input network connection settings and the connection status.

<Figure 4- 12> Example to View Network Connection

#### 4.3.2.3 Config Items

| Config Items contain server, time synchronization, network connection and settings as displayed in <Figure 4-13>. | <Figure 4- 13> Configuration Setting Item of Network Server |
| --- | --- |

1) Config Settings

The dialog box <Figure 4-14> appears using Config Server button to set server names and types, automatic server switching conditions, switching lists, etc.

<Figure 4- 14> Example for dialog box for Config Server

The server name is input with English or Korean alphabetic letter, numbers, etc. and the server type is chosen in Single, Dual Primary and Dual Secondary Server according to system installation state.  Select Automatic Server Switching Condition and Switching Lists when Dual Primary Server or Dual Secondary Server is set in server types and input communication ports in port settings to use between servers and clients.

Additionally, it is possible to specify whether to share the communication memory with network server programs depending on clicking on  in the following <Figure 4-14>.

| Reference) | Generally, the communication memory shares the memory with communication connection servers/ clients and network servers/clients is used for synchronization of servers, tag setting values and alarming. That is, servers and client systems are configured using communication servers / clients and network servers/ clients at the same time. |
| --- | --- |

2) Time Synchronization

Time Synchronization means that time for servers or client systems is synchronized at a specific time or manually by users.

Selecting Time Synchronization button brings up <Figure 4-15> as shown below.

<Figure 4- 15> Example of Dialog Box for Time Synchronization

If you click to check ‘Active’ (✔) button in <Figure 4-15> and set synchronization cycles (daily, hourly or minutely) or time, the entire system time (servers and clients) is synchronized to the set server time at any specified time.

The entire system time is synchronized to the current server time by pressing  in <Figure 4-15>.

3) Network Connection

Choosing Network Connection button from Configuration opens up the dialog box <Figure 4-16> to input the primary and secondary IP address of every server/client system connected.

<Figure 4- 16> Example of Dialog Box for Network Connection

The dialog box to modify (add) network node as shown <Figure 4-17> appears available to set names, the primary and secondary IP of the network node, whether to supply PLC_SCAN memory, etc. using  or  button in <Figure 4-16>.

<Figure 4- 17> Example of Dialog Box to Modify Network Node

Inputting all servers (including own IP address) and client IP address connected is required to synchronize tags, alarms, time, etc. in Network Connection Settings.

Also, set your own IP by clicking on  for your IP address.

#### 4.3.2.4 Window Menu Item

| Window Menu Items include sub menus such as Cascade, Tile Horizontally, Tile Vertically, Arrange Icons, Close and Close All displayed as <Figure 4-18>. These menus and MDI Windows have same instructions to use. | <Figure 4- 18> Window Menu Item |
| --- | --- |

#### 4.3.2.5 Help Menu Item

Help Menu Items contain sub menus for program information possible to check out the version information of the network servers.

## 4.4 Network Client

Network Client Programs interpret different data received from servers by connecting to network servers and transmit control commands sent from monitor programs to servers.

### 4.4.1 Running Network Client

Network client programs run as in the followings <Figure 4-19> by selecting ‘Network Client’ () button from AUTOBASE Window or Start Program, registering with monitor programs in Start Program, or using scripts in monitor programs.

The network client consists of the program name display, text menus, window internal areas, etc. and runs generally using shortcut keys.

<Figure 4- 19> Example of Running Network Client Program

### 4.4.2 Description for Each Text Menu

The text menu for the network client contains File, View, Config, Window and Help.

#### 4.4.2.1 File Menu Items

File Menu Items contain submenus to close the network client program.

#### 4.4.2.2 View Menu Items

| View Menu Items include submenus such as Servers, Communication Code, Network Connection as shown <Figure 4-20>. 1) Servers | <Figure 4- 20> View Menu Items for Network Client |
| --- | --- |

Clicking on ‘Servers’ button from View Menu displays the connection status of the connected network server, connected names, etc. in <Figure 4-19>.

2) Communication Code

If you select Communication Code button, you can see the window divided into two windows, transmitting and receiving code window. ‘Communication Code’ menu is used in network server/client programs as well.

<Figure 4- 21> Example to View Communication Code

3) Network Connection Status

Choosing ‘Network Connection’ button brings up <Figure 4-22> to display each primary and secondary IP or connection status input in network connection settings.

Also the menu is used in the network server/client programs, too.

<Figure 4- 22> Example to View Network Connection Status

#### 4.4.2.3 Config Menu Items

| The Config Menu Items consist of Config Settings, Network Connection and Settings as shown <Figure 4-23>. | <Figure 4- 23> Configuration Menu Items of Network Client |
| --- | --- |

1) Config Client

| Selecting ‘Config Client’ button from Configuration opens up the dialog box <Figure 4-24> available to set UDP/IP, TCP/IP communication service ports to communicate with servers, etc. | <Figure 4- 24> Example of Dialog Box for Config Client |
| --- | --- |

2) Network Connection

Input the primary and the secondary IP of every connected server/client in the dialog box <Figure 4-25> coming up using ‘Network Connection’ button from Config.

<Figure 4- 25> Example of Dialog Box for Network Connection

By pressing  or  button in <Figure 4-25>, the dialog box to add (modify) network nodes appears available to set names, the primary and the secondary IP of network nodes, whether to use PLC_SCAN memory supply, etc.

Input every connected server and client IP addresses in the dialog box, Network Connection Settings, to synchronize tag, alarms, time, etc.

Pressing  button sets my computer (Client) address with your own IP.

‘Network Connection Settings’ menu is used in Network Server / Client Programs as well.

| 3) Settings The dialog box <Figure 4-26> by clicking on ‘Settings’ button appears to set whether to switch the current tag values and alarm status values. Pressing ‘Exchange Tag Current’ buttons is to synchronize the current analog or digital tag values on the connected servers with the client ones. | <Figure 4- 26> Example of Dialog Box for Settings |
| --- | --- |

#### 4.4.2.4 Windows Menu Items

| Windows Menu Items for network clients contain submenus such as Cascade, Tile Horizontally, Tile Vertically, Arrange Icons and Close All and have same instructions with the own MDI Window manual. | <Figure 4- 27> Window Menu Items |
| --- | --- |

#### 4.4.2.5 Help Menu Items

Help Menu Items include submenus for program information available to check network client versions.

<Empty Page>

<Empty Page>

# Chapter5. SMS Manager

The SMS manager being used when necessary to transmit the alarm contents occurred to your cellular phone requires you to connect your cellular phones to computer serials or USB communication ports. Systems need to be connected to the internet in case of using voice messages and the following <Figure 5-1> is an example of running the SMS manager.

<Figure 5- 1> Example of Running the SMS Manager

## 5.1 Running the SMS Manager

Clicking on ‘SMS Manager’ () button from AUTOBASE Windows or the start program begins to run the message manager.

And this program can be run by registering with the monitor program together or using scripts after finishing all editing works.

## 5.2 Whole Figure and Shortcuts Descriptions

The SMS manager contains the program name display, text menus, Window internal areas, menu buttons, etc. and generally uses shortcut keys.

### 5.2.1 Figure Descriptions

Shortcut Descriptions as shown in <Figure 5-1> appear by running the SMS manager.

#### 5.2.1.1 Program Name Display

This is an original Windows feature to display names on the screen above.

#### 5.2.1.2 Text Menu

Text Menus including File, View, Config, Window and Help can be selected by pressing the left mouse button on the text you want to choose, or using arrow or ‘Enter’ key with holding’ ALT’ or ‘F10’ down.

#### 5.2.1.3 Menu Button

Menu Buttons are displayed under the screen of the SMS manager, etc. with texts.

#### 5.2.1.4 Shortcut Button

Shortcut buttons such as , , etc. are shown on the right screen.

#### 5.2.1.5 Windows Internal Area

Window Internal Areas displaying contents for the SMS manager are changed based on types of screens.

### 5.2.2 Shortcuts Descriptions

The following <Table 5-1> displays shortcut keys used in the SMS manager.

| Shortcut Keys | Description |
| --- | --- |
| ENTER | Select functions and check menus. |
| ESC | Cancel functions and Move back to previous menus. |
| ,,, (Arrow Keys) | Move between menus. |
| ALT, F10 | Move to text menus. |
| SHIFT+F5 | Arrange MDI Windows in cascade. |
| CTRL+F4 | Close currently selected MDI windows. |
| PGUP, PGDN, Other FUNCTION Keys | Used differently based on each screen. |
| Other Basic Shortcuts | Basic shortcut keys on Windows |

<Table 5- 1> Shortcut Keys for SMS Manager

## 5.3 Description for Each Menu Item

The Text Menu Items include File, View, Configuration, Help, etc.

### 5.3.1 File Menu Item

| The File Menu Items contain Send Manual Message, Test message, SMS Message Queue, Exit and current open Window buttons as displayed in <Figure 5-2>. | <Figure 5- 2> File Menu Items for SMS Manager |
| --- | --- |

#### 5.3.1.1 Send Manual Message

Clicking on Send Manual Message or  button opens up the dialog box <Figure 5-3> available to send messages using  button after selecting users and inputting sentences to send.

<Figure 5- 3> Example of Dialog Box to Send Manual Messages

#### 5.3.1.2 Send Test Message

| The dialog box <Figure 5-4> comes up by choosing Send Test Message button from Text Menu items. Sending test message is available by clicking on button after inputting Alarm Priority, Tag Types and Description, Message to send, etc. on the assumption that alarms would occur depending on the conditions mentioned above. | <Figure 5- 4> Example of Dialog Box to Send Test Messages |
| --- | --- |

#### 5.3.1.3 SMS Message Queue

This menu displays message contents left in the memory in order in the dialog box <Figure 5-5> available to check and cancel specific messages.

<Figure 5- 5> Example of Dialog Box to view SMS Message Queue

#### 5.3.1.4 Exit

You can close the SMS manager by selecting Exit button from File menu items.

#### 5.3.1.5 Open Windows Menu

Users are able to activate User Settings Screen, View Message Data and Communication Code, etc. by choosing open Windows below File menu.

### 5.3.2 View Menu Item

| Selecting View Menu brings up <Figure 5-6> containing menu items such as User Lists, Communication Code, SMS Called Lists, Web Service State and Main Program. | <Figure 5- 6> View Menu Items of the SMS Manager |
| --- | --- |

#### 5.3.2.1 User Lists

Click on ‘User Lists’ button from View Menu Items to display the dialog box <Figure 5-7> showing usernames, cellular phone numbers, status, retry count, etc.

<Figure 5- 7> Example of User Setting Screen

Double clicking on the left mouse button with selecting specific users in <Figure 5-7> brings up the user settings dialog box <Figure 5-8> possible to set whether to use user’s information, user names, phone numbers, sending conditions, Alarm Priorities to send messages, message type, etc.  Also, the SMS manager can set a maximum number of 256 users to receive messages.

<Figure 5- 8> Example of Dialog Box for User Settings

#### 5.3.2.2 Communication Code

<Figure 5-9> to display Communication Code appears by pressing Communication Code button from View menu items.

<Figure 5- 9> Example of Communication Code Screen

This Screen divided into the sending and the receiving code windows shows Communication Code sent to and received from cell phones in Hex, ASCII or Decimal format when the transmission system is set to be directly connected (Serials, etc.).

Also when you click on ‘Pause’ button, the display for viewing will pause.

#### 5.3.2.3 SMS Sended Lists

When you click on ‘SMS Sended Lists’ button from View menu items, it will show the display for viewing for each date as below <Figure 5-10>.

<Figure 5- 10> Example for Viewing Message Transmission Record

You can delete or print the records of specified dates using  or  button.

And setting font types and sizes to print is available by clicking on  as well.

#### 5.3.2.4 Web Service State

Web Service State appears as in the following <Figure 5-11> by clicking Web Service State button.

<Figure 5- 11> Example of Viewing Web Service State

Site names in <Figure 5-11> show the primary and the secondary sites to transfer web service messages set in ‘Config | Communication Port Settings’.

#### 5.3.2.5 Main Program

Users are able to move Windows focus to the Main program or run it by choosing ‘Main Program’ button from View menu items.

### 5.3.3 Config Menu Item

| This menu items include user settings, alarm priority settings, message format, communication port settings, settings as displayed in <Figure 5-12>. | <Figure 5- 12> Configuration Menu Item of SMS Manager |
| --- | --- |

#### 5.3.3.1 User Settings

The dialog box <Figure 5-13> as below to show 256 users’ names and setting state appears using User Settings button.

Double clicking the left mouse button with selecting users in <Figure 5-13> or pressing  button, the dialog box <Figure 5-8> comes up to set whether to select users, user names, cell phone numbers, transfer conditions, alarm priority to send messages, etc.

<Figure 5- 13> Example of Dialog Box to Select Users in Settings

#### 5.3.3.2 Alarm Priority Settings

Pressing the Alarm Priority Settings button from Config menu items brings up <Figure 5-14> to set the alarm priority for each user.

<Figure 5- 14> Example of Dialog Box to Set Alarm Priority

The message manager sends text messages to relevant user cell phones when priority alarms occur specified in the monitor program (Depending on user settings, DI tag values may need to be ON together.) and alarm priorities for specific users are set in <Figure 5-14>.

#### 5.3.3.3 Message Format

<Figure 5-15> comes up by choosing Send Message Format button from Configuration Menu Items to set messages to send.

<Figure 5- 15> Example of Dialog Box to Set Message Formats

There are two types of settings in send messages format. : Default and User Defined.  The default settings process ‘send messages’ in the order of time, tag comments and messages.  Users are able to input directly ‘send messages’ in edit boxes and each button to edit message contents in User Settings. Help displays how to input ‘send message’ in detail.

#### 5.3.3.4 Communication Port Settings

Clicking ‘Communication Port Settings’ button brings up the dialog box <Figure 5-16>.

<Figure 5- 16> Example of Dialog Box to Set Transmit Systems

You set message transfer systems by setting transfer system type including ‘direct’, ’web service’ and ‘transmit to server(server/client structure)’, serial ports/ speed, network settings, web service, etc. in <Figure 5-16>.

#### 5.3.3.5 Settings

You can set retrial times, delay time, maximum number of characters to send, message type, phone numbers to receive messages, PCS model, etc. for message systems in <Figure 5-17> appearing by clicking ‘Config’ button from Configuration Menu items.

Do not input anything or input cellular phone numbers connected to the system for phone numbers to receive messages.

<Figure 5- 17> Example of Dialog Box for Settings

### 5.3.4 Windows Menu Item

| This menu items contain submenus such as Cascade, Tile Horizontally, Tile Vertically, Arrange Icons, Close and Close All and have a same instruction with the original MDI Windows function. | <Figure 5- 18> Windows Menu Item |
| --- | --- |

### 5.3.5 Help Menu Item

You can check the version information by clicking on ‘About’ item for SMS manager from Help menu items.

<Empty Page>

# Chapter 6. Line Printer Manager

Line Printer Manager usually use dot printers to print directly alarms raised in the monitor program to printer porters. The following <Figure 6-1> displays line printer manager running.

The <Figure 6-1> displays line printer manager running.

<Figure 6- 1> Line Printer Manager Running

## 6.1 Running Line Printer Manager

Clicking on ‘Line Printer Manager’ () button makes Line Printer Manager run. Also, after editing, you can run this by registering with monitor programs in Window Start Program or using scripts in monitor programs.

## 6.2 Whole Figure and Shortcuts Descriptions

Line Printer Manager contains program name display, Internal Windows and program menu options such as File, Config, and Help.

The internal Windows displays the setting status and numbers of remaining alarms to print of Line Printer Manager as shown <Figure 6-1>.

The following <Table 6-1> shows the shortcut keys used in Line Printer Manager.

| Shortcuts | Functions |
| --- | --- |
| ENTER | Select functions and check menus. |
| ESC | Cancel functions and move to the previous menus. |
| ,,, (Arrow Keys) | Move the internal Window up/down/ left/ right or between menus. |
| ALT, F10 | Move to the menu bar. |
| ALT+F4 | Close programs. |
| Windows Default Shortcuts | Default shortcuts functions |

<Table 6- 1> Shortcuts Descriptions of Line Printer Manager

## 6.3 Descriptions for Each Menu

The menu bar under Line Printer Manager contains File, Config and Help menu.

### 6.3.1 File Menu

File menu has a submenu available to exit.

| 6.3.2 Config menu The Config Menu contains submenus named Port Settings, Display Formats and Control Commands as shown <Figure 6-2>. | <Figure 6- 2> Configuration Settings Menu |
| --- | --- |

#### 6.3.2.1 Port Settings

Clicking on port settings menu from Config opens The Port Settings dialog box in the following <Figure 6-3> to set whether to print, how to print dates, ports and speed with timer.

<Figure 6- 3> Example of Dialog Box for Print Port Settings in Line Printer Manager

#### 6.3.2.2 Display Formats

<Figure 6-4> appears by selecting ‘Display Formats’ menu.

There are Default and User Defined in Display Format.  ‘Default’ setting is configured to set the intervals in order of dates, time, tags and tag explanation.  Or you are able to set the interval by inputting the contents to print in the editor box by using , , , , , ,  buttons

<Figure 6- 4> Example of Dialog Box for Printing Interval Settings

#### 6.3.2.3 Control Commands

Setting ‘Control Commands’ (ESC Control Commands) helps you print alarms with different colors to the color printer, or change the font or font size according to each alarm type.

Use <Figure 6-5> below to set the command.

For more information about how to input the control commands, refer to the instruction manual provided when buying printers.

<Figure 6- 5> Example of Dialog Box for Control Commands Settings for Each Alarm Types

### 6.3.3 Help Menu Items

Help Menu Items contain the submenu named ‘About’ to check the Line Printer Manager version.

<Empty Page>

# Chapter 7. Watchdog

‘Watchdog’ is created to run specific programs again in case programs would be closed due to bugs, program instability, etc.  <Figure 7-1> displays the watchdog running.

<Figure 7- 1> Watchdog Program Running

## 7.1 Run Watchdog

Select and run the ‘watchdog’ () in AutoBase Window or Start Program.

You can run the ‘watchdog’ by registering it in Start Program after editing or using the scripts of Monitor Program.

## 7.2 Whole Figure and Shortcuts Descriptions

Watchdog consists of the program display, menu bars, internal Windows, etc. and displays program names to use as watchdog, set points, current values, program start time and  whether to use functions or not.  The following <Table 7-1> shows shortcut keys available in watchdog.

| Shortcuts | Functions |
| --- | --- |
| ENTER | Select functions and Check menus, etc. |
| ESC | Cancel functions and move to the previous menus |
| ,,, (arrow keys) | Move the internal Window up/down/ left/ right or between menus |
| ALT, F10 | Move to text menu |
| ALT+F4 | Close Programs |
| Default shortcuts for Windows | Default shortcuts for Windows |

<Table 7- 1> Shortcuts Summay for Watchdog

## 7.3 Menu Bar Description

The menu bar includes File and View.

### 7.3.1 File Menu

The File Menu contains the submenu ‘Exit’ available to close the watchdog program.

### 7.3.2 View Menu

The View Menu incluses submenus such as Log File and Hide as below.

<Figure 7- 2> Watchdog View Menu Items

#### 7.3.2.1 Log List

Choose ‘Log List’ from View Menu to check logged informtation of the Watchdog program in Notepad in the following <Figure 7-3>.

<Figure 7- 3> Example to View Log File in Watchdog

#### 7.3.2.2 Hide

You can hide the Watchdog Program by clicking on ‘Hide’ option from View Menu.

Selecting  icon in your system tray on Windows displays the Watchdog program again.

## 7.4 Shortcut Menus

Shortcut menus such as ‘Run Program’ and ‘Properties’ options appear as below <Figure 7-4> by clicking on the right mouse button on the program registered in Watchdog.

<Figure 7- 4> Watchdog Shortcut Menu

### 7.4.1 Run Selected Programs

Pressing the selected programs from the shortcut menu is available to run each one registered in Watchdog.

### 7.4.2 Modify Properties

Select ‘Modify Property’ option from the Shortcut Menu to open up the dialog box to modify properties in the following <Figure 7-5> available to set timer and whether or not to be active of Watchdog functions.

<Figure 7- 5> Example of the Dialog Box to Modify Properities of Watchdog

<Empty Page>

<Empty Page>

# Chapter 8. Running Server

Selecting ‘Running Server’ program makes it possible to save data, Integrate database, share servers, etc. and the following <Figure 8-1> displays the home screen.

<Figure 8- 1> Home Screen of Running Server

## 8.1 Running Server

Clicking on ‘Running Server’() button is available to run Running Program in Windows or Start Program.

Register ‘Running Server’ in Windows or Start Program or use scripts in the monitor program to run it.

### 8.2 2 Whole Figure and Shortcuts Descriptions

‘Running Server’ program is made up of the program display, menu bars, internal Windows, etc. and is generally used with shortcut keys as shown in <Table 8-1>.

| Shortcuts | Functions |
| --- | --- |
| ENTER | Select functions and Check menus, etc. |
| ESC | Cancel functions and move to the previous menus |
| ,,, (arrow keys) | Move the internal Window up/down/ left/ right or between menus |
| ALT, F10 | Move to the menu bar |
| ALT+F4 | Close Programs |
| Default shortcuts for Windows | Default shortcuts for Windows |

<Table 8- 1> Shortcuts Descriptions of Watchdog

## 8.3 Menu Bar Description

The menu bar under ‘Running Server’ program contains File, View, Config and Help menu.

### 8.3.1 File Menu

The File Menu has a submenu, ‘Exit’, to close the running server.

### 8.3.2 View Menu

| The View submenu contains items such as DB Integrations and Shared Server Status as displayed in <Figure 8-2>. | <Figure 8- 2> View Submenus of the Running Server program |
| --- | --- |

#### 8.3.2.1 DB Integrations

‘DB Integrations’ is to calculate and display integral values of data, saved in database data, for previous and this year/month/day and time.

Selecting ‘DB Integration’ item from View Menu shows DB Integral Values for lists registered in <Figure 8-3>.

<Figure 8- 3> Example of Dialog Box to View DB Integration Values

Clicking on ‘File | List Settings’ in <Figure 8-3> opens the dialog box <Figure 8-4> to add or delete some data to display DB Integration.

<Figure 8- 4> Example of Dialog Box to set lists of DB Integration

The dialog box <Figure 8-5> appears by clicking on  button from <Figure 8-4>.

<Figure 8- 5> Example of Dialog Box to Add Lists of DB Integration

DB Integration Lists can be added by selecting saved lists and integration tags in <Figure 8-5>. Saved List and Integration Column are configured from ‘Config | Database’ menu.

Select  button from <Figure 8-4> to delete the DB Integration lists from settings.

#### 8.3.2.2 Shared Server Status

Shared server is a configuration designed for sharing data such as current values of systems connected via network. Select shared server from view for a dialog box as in <Figure 8-6> to view web server/client, network server/client status in connected IP address, send/receive frame rate and other values.

Service port to be used for shared server is configured from ‘Config | Shared Server’ menu.

<Figure 8- 6> Dialog box to view shared server status

### 8.3.3 Configuration Settings Menu

| Configuration menu items of the program consist of submenus in Database, Config Excel Path, and Shared Server as shown in <Figure 8-7>. | <Figure 8- 7> Configuration menu items |
| --- | --- |

#### 8.3.3.1 Database

Config | Database menu consists of Connection String, and Save Lists.

1) Connection String

Connection Strings is a configuration required for storing monitored data to database or to view as Excel format reports.

Select Config | Database | Connection String menu for a configuration dialog box as in <Figure 8-8> where connection string which can be used for ‘saving to database’ functionality or others can be added, modified and/or deleted.

<Figure 8- 8> Dialog box for database connection string configuration

Selecting ,  buttons from <Figure 8-8> prompts a dialog box shown as <Figure 8-9>, where Connection String can be added or modified.

Select  from <Figure 8-8> in order to delete a specific Connection String.

For Connection String to be entered in <Figure 8-9>, please refer to the Connection String example figure or database manuals of the DB vendors.

<Figure 8- 9> Dialog box to manage DSN

2) Saved lists

Saved Lists is a configuration designed for storing monitored data into the database in the predefined time interval.

Select Config | Database | Save Lists menu for a dialog box shown as in <Figure 8-10>.

<Figure 8- 10> Dialog box to configure database save list

Selecting ,  buttons from <Figure 8-10> prompts a dialog box shown as <Figure 8-11>, where save lists can be added or modified.

Select  from <Figure 8-11> in order to delete a specific list.

<Figure 8- 11> Dialog box and saved list tab for configuring database saved list

<Figure 8-11> is a saved list tab for saved list configuration setting dialog box, and the following contents as shown in <Table 8-2> are entered.

| Saved list | Description |
| --- | --- |
| Title | Name for saved list is entered using alphabet letters and numbers. |
| DSN | Connection String name configured is entered using the combo box. |
| Table | Table name to store data is entered. |
| Data Cycle | Storage interval is configured in millisecond units. Normally 1 minute, or 1 hour is used. |
| Use storage timing | Store data at the time of storage. Example) Data generated at 1200 are normally stored in 1300 therefore data generated at 1300 are also stored. |
| Use duplex server for saving | In case monitoring/controlling systems are configured in duplex fashion, and there is one database server, only the main server will be handling for storage using this option. |
| Relative generation | Database in the higher time unit of the above configured time interval is relatively generated. Example) When the storage interval is set to 1 minute and Relative generation is selected, monitoring data is stored in 1 minute interval and when the storage interval is changed to 1 hour, relative generation table will store data generated in 1 hour. |

<Table 8- 2> Elements of the saved list tab of saved list configuration dialog box

Selecting Date Column tab from saved list configuration settings dialog box will appear a dialog box shown as in <Figure 8-12>.  Enter in date column and MilliSec (Millisecond) column name here.

<Figure 8- 12> Date column tab from database saved list configuration settings dialog box

Selecting tag list tab from saved list configuration settings tab will display a dialog box shown as in <Figure 8-13>.

<Figure 8- 13> Tag list tab of database saved list configuration tab

Selecting  button from <Figure 8-13> will display tag selection dialog box, here select tags to store to database to add a saved list with the column name from the tag name. Select the added saved list to modify column name, and data type to store where data types include current value(analog, digital), least value(analog), highest value(analog), integration value(analog), average value(analog), on hour(digital), and off hour(digital).

#### 8.3.3.2 Config Excel Path

Excel application path for excel script and reports is configured in Excel path configuration.

Select Config | ‘Config Excel Path’ for a dialog box shown as in <Figure 8-14>.  Enter in the path of excel application executable file from this dialog box.

<Figure 8- 14> Excel path configuration dialog box

#### 8.3.3.3 Shared server

Shared server is a configuration setting used to store current value of the connected systems via network and other values.  Select shared server menu from configuration settings for a dialog box shown in <Figure 8-15> where service port number is entered.

Connection status of the shared server can be viewed from ‘View | Shared Server’ menu.

<Figure 8- 15> Shared server configuration dialog box

### 8.3.4 Help text menu

Help text menu of the program includes help submenu.

Select help submenu to view application program related references.

<Empty Page>

# Chapter9. Configuration for Web server connection

Web server is a program which allows monitoring and control of the automated field under inspection through internet and intranet environment.

Network for web server application is composed of a server which provides services, and web client, which connects via internet and intranet for control and monitoring.

Web server connection configurations refer to system configurations of clients, which connect to server for control and monitoring.

※ Note) Usage of web client, which connects to web server for monitoring and control, is similar to other generic monitoring programs.  Please refer to program manual or help contents for detailed usage.

## 9.1 System requirement

The system requirements of web client for web server connection is as in the following table <Table 9-1>.

| System : | Pentium 4 1.8 or higher, and least 512M of main memory, storage device with 200M or more space (HDD). |
| --- | --- |
| Operating System : | Windows 98/me/2000/XP/Server2003 or newer (2000/XP or newer operating system recommended. |
| .NET Framework 1.1 or higher |
| Microsoft Internet Explorer 6.0 or higher. |

<Table 9- 1> System requirement for web client

## 9.2 Installation of .NET Framework

Web server / client is developed using .NET, a new breed of technology from Microsoft, and requires .NET Framework installation (1.1 or higher version) in Windows 98/me/2000/XP/ Server2003 and other newer Windows operating system.  (2000/XP or newer Windows operating system is recommended)

.NET Framework 1.1 installation package can be obtained in following manners.

( Free download from Microsoft website.

( Download from autobase.biz site.

( From the distributed CD in REDIST\DotNetFramework_1_1\dotnetfx.exe.

## 9.3 Security settings

In order to execute service contents provided by web server, or perform tasks such as monitoring and controlling, registration as an assembly trusted, or a trusted site must be performed.

※ Note) All internet applications running under Microsoft .NET framework require security settings as mandatory.

### 9.3.1 Registering as a trusted site

In order to register as a trusted site, the following two configurations must be performed.

( .NET Security control

( Register as a trusted sites in Internet Explorer

#### 9.3.1.1 Adjust .NET Security

| After Microsoft .NET Framework installation, select Control Panel¦Administrative tools (in 98/me, select Programs¦Administrative tools) and check for .NET Framework Wizards. Run .NET Framework Wizards for a window shown as in <Figure 9-1>. | <Figure 9- 1> .NET Wizards window |
| --- | --- |
| ※ Note) | In case each of the items in <Figure 9-1> are displayed in English, go to Windows Update website, download and install .NET Framework version 1.1 Korean Language Pack’ for Korean menu items. |

Select <Figure 9-1> ‘Adjust .NET Security’ for a dialog box as shown in <Figure 9-2>.

Select ‘Make changes to this computer’ in <Figure 9-2> and press  button for a dialog box in <Figure 9-3>.

<Figure 9- 2> Security policy dialog box in Security Adjustment Wizard

<Figure 9- 3> Security Adjustment Wizard dialog box

From Security Adjustment Wizard dialog box in <Figure 9-3>, select ‘Trusted Sites’ and set to ‘Full Trust’ from the level of trust, and select  button for a screen similar to <Figure 9-4>.

In a dialog box which displays the configured security level as in <Figure 9-4>, click on  button to complete security adjustment for.NET.

<Figure 9- 4> Security Adjustment Wizard completion dialog box

#### 9.3.1.2 Register as a Trusted Site in Internet Explorer

After security adjustment is performed with .NET Framework Wizards, run Internet Explorer and select ‘Tools|Internet Options’ for an Internet option configuration dialog box.  Select ‘Security’ tab from Internet Options for a following dialog box <Figure 9-5>.

<Figure 9- 5> an example of Internet Explorer option dialog box with Security tab on

Select Trusted sites from dialog box in <Figure 9-5> and select  button for a dialog box as shown in <Figure 9-6>.

<Figure 9- 6> Trusted sites dialog box from Internet Options in Internet Explorer

Enter in the IP address or web site name of desired site from <Figure 9-6> and enter  button for site registration.

※ Note) Generally, when registering as a trusted site from <Figure 9-6>, ‘Require server verification (https:) for all sites in this zone’ (  ) should be left unchecked.

### 9.3.2 Trust an assembly

After Microsoft .NET Framework installation, select Control Panel | Administrative tools (in 98/me, select Programs | Administrative tools) and check for .NET Framework Wizards. Run .NET Framework Wizards for a window shown as in <Figure 9-1>.

Select ‘Trust an assembly’ from <Figure 9-1> for a dialog box as shown in <Figure 9-2>.

Select ‘Make changes to this computer’ in <Figure 9-2> and press  button for a dialog box in <Figure 9-7>.

<Figure 9- 7> Assembly selection dialog box in Trust an Assembly window

Enter in an assembly path or URL from <Figure 9-7> and select  button for a dialog box as shown in <Figure 9-8>.

<Figure 9- 8> Assembly selection dialog box

Select ‘Apply to all assemblies sharing a common key’ from <Figure 9-8> and leave ‘Include version number’ unchecked and select  button for a dialog box as shown in <Figure 9-9>.  With ‘Include version number’ checked, monitoring/controlling for web client is only available for the selected version.

<Figure 9- 9> Assembly trust level selection dialog box from Trust an Assembly window

From <Figure 9-9>, select ‘Trusted Sites’ and set to ‘Full Trust’ from the level of trust, and select  button for a screen similar to <Figure 9-10>.

In a dialog box which displays the configured security level as in <Figure 9-10>, click on  button to complete security adjustment for.NET.

<Figure 9- 10> Trust an Assembly Wizard completion dialog box

<Empty Page>

<Empty Page>

INDEX

A~B

Adjust .NET Security	199

alarm	157, 173

Alarm Color	96

Alarm Events	72

Alarm Files	70

Alarm List View	71

Alarm Priority Settings	168

Alarm Window	22

Analog	9

Analog Data View	48

Analog Input Details	44

Analog Inputs	40

Analog Meta	11

Analog Output Details	53

Analog Outputs	51

Analog Rectangle	10

Analog Rotation	13

Analog Status	12

Analog Text	10

Analog Trend Diagnosis	46

Animation	33

Animation Editor	15

Automatic Report Print	102

Background Bitmap	37

Background Color	37

Basic Color	95

Bit Write	113

Bitmap	32

button	17

C~D

change digital input values	14

Check Box	28

Circle	35

Client State	143

Clock	36

Color	95

Combo Box	28

Communication Code	144, 151, 164

Communication Code into ASCII	116

Communication Code into Hex	116

Communication Port Settings	169

Communication Server	78, 107

Communication Setting Method	123

Communication Settings	126

Communication Status Signal	132

Computer Duplex	130

Config	94

Config Alarm	94

Config Client	153

Config Colors	95

Config Data	96

Config Excel Path	99

Config Font	95

Config Menu Item	120

Config Other	98

Config Settings	146

Config Users	97

Configuration for Web server connection	197

Connection String	100, 189

Control Commands	176

Curve	36

Database	29, 100

Database Trend	31

Date	37

DB Integrations	86

Demand Controls	80

Demand Window	26

Detailed View of the Registered Group	69

Device	123

DEVICE	128

Device Settings	128

Dialup Settings	129

Digital	14

Digital Animation	15

Digital Circle	16

Digital Data View	60

Digital Input Details	56

Digital Inputs	54

Digital Output Button	19

Digital Output Details	64

Digital Outputs	62

Digital Rectangle	16

Digital Text	17

Digital Trend Diagnosis	58

Display Changes	32

Display Formats	176

DLL Protocol Information	119

E~K

Edit Box	28

Editor Font	121

Entire Tags	38

Exit	93, 114, 162

Exit Communication Program	114

Extension of Graphic Element	37

FieldBus	125

File Menu	88, 111

General Outlines of Execution Program	1

Graphic Module	21

Group	37

Help	104

Help Menu	121, 171

Images	32

Internal Computer Card	125

Keylock Information	105

L~N

Line	35

Line Duplex	130

Line Print Manager	173

List Box	28

Log Files	74

Log In	88

Log List View	75

Log Out	89

Main Program	115, 166

Memory	115

Menu	88, 111, 141, 150, 158, 160, 175, 180, 186

Menu Bar	7, 109

Menu Button	7, 109, 158

Message Format	168

Milli-Data Window	27

Milli-Datas View	81

modem connection	133

Modem Options	121

Modify Communication Ports	111

Module Hide Button	18

Module Selection Button	17

Monitor Program	5

Multi-graph	23

MultiPort MultiTasking	120

Multi-trend	24

Navigation	87

Network	125, 135

Network Client	150

Network Connection	145, 148, 153

Network Connection Status	152

Network Memory Client Settings	138

Network Memory Server	117

Network Memory Server / Client	135

Network Memory Server Settings	136

Network Program	135

Network Server/Client Configuration	139

O~S

OPC	125

Open Windows Menu	162

Options	120

phone number to receive message	170

PLC_SCAN.EXE	107

Polygon	36

Port Status	117

Primary	140

Print Screen	91

ProfiBus	125

Protocol Settings	129

Radio Button	28

Read Memo	90

Real-time Test Graph	30

receiving code window	164

Rectangle	34

Reports	78

reserve/basic device conversion	133

retrial times	170

Rounded Rectangle	36

Run Monitor Program	5

Run Studio	93

Running Server	185

Save Screen	91

Save Selected Screen	92

Saved lists	190

Schedules	83, 102

Script	37

Script Button	19

Scripts	76

Secondary	140

Security Adjustment	199

Security settings	198

Send Manual Message	160

Send Message Queue	161

Send Test Message	161

sending code window	164

Serial	123

Server State	142

Servers	151

Set Local	153

Set Read Method	131

Settings	154, 170

SetVipScan	120

Shared Database	101

Shortcut Button	158

Shortcut Menus	182

Shortcuts	7, 110, 159

Single line text	34

SMS Manager	157

SMS Sended Lists	165

Stand Alone	140

String Tag	20

String Tags	65

System Memory	142

T~Z

TCP/IP	125

The Shutdown Privilege	93

Time interval	33

Time Synchronization	147

Title Bar	6

Trust an assembly	204

Trusted Sites	202

UDP/IP	125

User Lists	162

User Settings	167

UserName	104

Using Start Program	6

View	93

View Graphics	8

View Menu	8

View Menu Items	114

View Registered Groups	67

VipScan	120

Virtual Write	114

Watchdog	179

Web Service State	166

Window Control	28

Windows Menu	103

Windows Menu	121

Windows Menu	171

Word Write	113

Write Memo	89

XY Graph	30

Others

.Net Framework	198